## Slide 1: ESE532: System-on-a-Chip Architecture
Day 13: October 14, 2024
Vitis OpenCL
Data Transfer Model

## Slide 2: Previously
Value of small, local memories
Tune local memories in C
DMA as data-movement threads

## Slide 3: Today
Vitis/OpenCL Interface
Execution Model (Part 1)
Host-Side Programming (Part 2)
FPGA-Side Programming (Part 3)

## Slide 4: Message
Vitis uses an explicit DMA transfer interface
Can build our streaming model on top of primitives offered
Will need to tune parameters and use carefully to get maximize performance
  Good and bad  largely exposed

## Slide 5: Execution Model(s)
Part 1

## Slide 6: Model
Host and Accelerator
Host control
  Set accelerator arguments
  DMA bulk data to and from accelerator
  Tell it to start
  DMA, Accelerator runs as independent thread
  Synchronize on data return

## Slide 7: Remember: Preclass 4a
Where do we set DMA arguments?

## Slide 8: Remember: Preclass 4a
Set arguments to accelerator
Accelerator
Uses to
grab inputs

## Slide 9: Programmable SoC
UG1085
Xilinx
UltraScale
Zynq
TRM
(p27)

## Slide 10: Function Call
Host and Accelerator
Host control
  Set accelerator arguments
  DMA bulk data to accelerator
  Tell it to start
  DMA result back
  Host program wait on accelerator completion

## Slide 11: Separate Accelerator Thread
Host and Accelerator
Host control
  Set accelerator arguments
  Tell it to start
    accelerator
      DMA bulk data to accelerator
      DMA result back
    Host: execute something else
  Host program synchronize before use accelerator result

## Slide 12: PS<->PL Interface
Xilinx UG1393, Fig. 2 (Ch. 3)
Part 2
Part 3

## Slide 13: Minimal
Simple case one host process, one accelerator

## Slide 14: Accelerator Stream
Dataflow stream accelerators on host side

## Slide 15: Streaming
Map general streaming
Use multiple threads
  Even processors

## Slide 16: Streaming
Map general streaming
Use multiple threads
  Even processors
… and multiple accelerators
Given space, any streaming case
  DMA buffers cross PS<->PL

## Slide 17: Data Movement (Options)
Access from global memory
Configure DMA/accelerator with main-memory pointer
DMA copy into BRAM memories
  Built on top of other with DMA copy loop

## Slide 18: Data Movement (Options)
How copy loop improve performance?
  Assume dataflow streaming between copy loop and accelerator computation?

## Slide 19: Remember: Preclass 4a

## Slide 20: Copy Loop Benefits
Run concurrently – improve throughput
  Overlap compute and communication
Hide latency of read

## Slide 21: Host-Side Programming
Part 2

## Slide 22: Outline
Platform
Device
Context
Command Queue
Load FPGA
Buffers and Transfer
Kernel Execution
Synchronize on Result
Overlap Data and Compute
Running Multiple Kernels

## Slide 23: Platform
For general case where have multiple OpenCL platforms
Silly for Ultra96 SoC
  and, looks like we can partially hide

## Slide 24: Device
For case of multiple FPGAs  which FPGA
Also somewhat silly for Ultra96 with single FPGA (PL)
Amazon F1.x16large has multiple FPGAs

## Slide 25: Device
Our Utilities.cpp,h – hide Platform
  std::vector<cl::Device> devices = get_xilinx_devices();
  devices.resize(1);
  cl::Device device = devices[0];
Get away with simplification
  Know want only Xilinx platform
  Know only one device (Ultra96)

## Slide 26: Context
Context for device
  Not sure what flexibility/differentiation this is giving
    maybe for DFX overlay shells
  Supports some error callback

## Slide 27: Command Queue
Creates a queue that holds commands
Commands govern host and kernel interactions
Commands in the queue run in separate thread than main host code.
  Commands don’t necessarily execute immediately after they are placed into the queue

## Slide 28: Command Queue (cont.)
Two types of queues: in-order and out-of-order.
  In order queues execute commands in the order that they are placed into the queue. Next command waits until previous command finishes.
  Out-of-order queues execute commands in the queue in an order that is constrained by synchronization flags. Commands don’t need to wait until previous commands finish.

## Slide 29: Load Bitstream on FPGA
Where we actually reconfigure FPGA
  Not really for our current platform
    But confirms bitstream using
    …and needs read some information from xclbin
  For Partial Reconfiguration (DFX) platform
    Option to choose which to load
    Option to reconfigure during operation under host control
      not one we’ll exercise this term

## Slide 30: Kernels
Setup the actual accelerators to call
  Extract handle to reference them from the loaded bitstream (program)
  Just naming them at this point

## Slide 31: Preclass 1
Kernel with
  10ms input transfer
  30ms compute
  5ms outputs
Latency?
Throughput if must serialize?
Throughput if overlap data transfers and computation?

## Slide 32: Preclass 1

## Slide 33: Host and Device Memory View
Host pointers not necessarily meaningful to device
  Need to map
  Different memories? (depend on platform)
    Embedded incl. Ultra96 (same), data-center (may be different)
  Virtual vs. Physical addresses?
  Same memory, different address map?

## Slide 34: Buffers and Transfer
Create
Buffers
Set kernel
pointers
Host side pointers
Fill with host data
Launch data transfer
(enqueue)

## Slide 35: Remember: Preclass 4a
clSetKernelArg
Use
dev_mem_ptr

## Slide 36: Movement Options
clEnqueueReadBuffer (WriteBuffer)
  Not guarantee timing of transfer
clEnqueueMigrateObjects
  Supports overlap of compute and communicate
  recommended

## Slide 37: Buffers and Transfer
Create
Buffers
Set kernel
pointers
Host side pointers
Fill with host data
Launch data transfer
(enqueue)
Done once
For startup
After first, overlap

## Slide 38: Remap Device Pointer
Migration remap dev_mem_ptr
(don’t know if this is happening this way)

## Slide 39: Kernel Invocation
After
  Kernel arguments set
  Buffer transfers have been enqueued
Causes to actual run on data transferred
Commands – command queue
Kernel – naming of kernel to run

## Slide 40: Synchronization
Synchronization needed between main host code thread and the command queue which operates asynchronously
Also needed to constrain command execution order in out-of-order command queue

## Slide 41: Synchronization (cont. 1)
Synchronization utilizes OpenCL event object:
// single event flag
cl::Event flag;
// vector of event flags
std::vector<cl::Event> wait_list;
// To add an event flag to the wait_list, do:
wait_list.push_back(flag);

## Slide 42: Synchronization (cont. 2)
Commands can be issued without synchronization, like so:
q.enqueueMigrateMemObjects({in1_buf, in2_buf}, 0);
q.enqueueTask(krnl_mmult);

## Slide 43: Synchronization (cont. 3)
Or with synchronization:
cl::event flag0;
cl::event flag1;
std::vector<cl::event> wait_list;
// Move memory to FPGA, and signal fla0g event when done.
q.enqueueMigrateMemObjects({in1_buf, in2_buf}, 0, NULL, &flag0);
// Add the flag to the wait_list
wait_list.push_back(flag);
// Run the kernel only after all the events in the wait list have triggered
// and trigger &flag1 when done
q.enqueueTask(krnl_mmult, &wait_list, &flag1);
// Make the host code wait here until flag1 is triggered.
clWaitForEvents(1, (const cl_event *)&flag1);

## Slide 44: Preclass 2a
Break kernel into three 10ms pieces and use dataflow between them
  10ms input transfer
  10ms compute x 3
  5ms output transfer
Throughput?

## Slide 45: Preclass 1 and 2

## Slide 46: Dataflow: Host-to-kernel
Create a dataflow stream between host process and accelerator
  Like DATAFLOW pragma
  Control on FPGA/kernel side (coming up)
Overlap next computation (setup) on host with FPGA kernel
UG1393 says embedded platforms not support?
  …but maybe not need since single global memory

## Slide 47: Preclass 2b
How many additional inputs send before get associated output? (pipeline depth)

## Slide 48: Kernel Completion/ Synchronization
Don’t have to synchronize right after an operation
Can have several in flight (in pipeline)
Synchronize only after sending several (pipeline depth) inputs

## Slide 49: Overlapping Data and Compute
Use control of when synchronize to overlap data and compute
Start (queue up) next data transfer and invocation before dataflow pipeline finishes
Need to reason about (or experiment with) how many to in flight
  When to synchronize

## Slide 50: Running Multiple Kernel Instances
Can have multiple instances of same kernel on FPGA
Dispatch from Out-of-Order command queue
Will distribute among identical kernels
Out-of-Order queue
  May also help with compute/communication overlap for single kernel?

## Slide 51: Parallelism
Pipeline/Dataflow
  With Host Dataflow
  DMA transfers and compute
  Within compute
Thread Parallelism
  Launch multiple accelerator
Data Parallelism
  Define multiple instances of one accelerator and enqueue work for

## Slide 52: Cleanup
Need to release/free resources setup

## Slide 53: FPGA-Side Programming
Part 3

## Slide 54: Interface Pragmas
Assign AXI
  Bundles
Host-to-Kernel
Burst read
Interface width

## Slide 55: Programmable SoC
UG1085
Xilinx
UltraScale
Zynq
TRM
(p27)

## Slide 56: Programmable SoC
AXI Channels
128b wide
@ 333 MHz
=5.3GB/s

## Slide 57: AXI Channels
Can tell it to use AXI Channels
By default (as shown above) all share same channel

## Slide 58: AXI Channels
Separate names to use different
Note, not naming to match ZCU3EG names
  Portability across targets

## Slide 59: Programmable SoC
AXI Channels
128b wide
@ 333 MHz
=5.3GB/s

## Slide 60: Older and Defaults
2019.2:
#pragma HLS INTERFACE s_axilite port = in1 bundle = control
#pragma HLS INTERFACE s_axilite port = in2 bundle = control
#pragma HLS INTERFACE s_axilite port = out_r bundle = control
#pragma HLS INTERFACE s_axilite port = size bundle = control
#pragma HLS INTERFACE s_axilite port = return bundle = control
#pragma HLS INTERFACE m_axi port=in1 offset=slave bundle=gmem
#pragma HLS INTERFACE m_axi port=in2 offset=slave bundle=gmem
#pragma HLS INTERFACE m_axi port=out_r offset=slave bundle=gmem
2020.1:
#pragma HLS INTERFACE m_axi port=in1 bundle=gmem
#pragma HLS INTERFACE m_axi port=in2 bundle=gmem
#pragma HLS INTERFACE m_axi port=out_r bundle=gmem

## Slide 61: Remember: Preclass 4a
S-AXI Control – load pointers
M-AXI transfer
Using pointers

## Slide 62: Host-to-kernel Dataflow
ap_ctrl_chain

## Slide 63: Burst Transfer
Where have we seen this before?

## Slide 64: Remember: Preclass 4a

## Slide 65: Burst Transfer
Use Dataflow to setup as separate threads on accelerator side
Believe this is way to burst copy into local memory

## Slide 66: Data Movement (Options)
Access from global memory
Configure DMA/accelerator with main-memory pointer
DMA burst copy into BRAM memories
  Built on top of other with DMA copy loop

## Slide 67: Preclass 3, 4
333MHz cycle time on bus
Peak bandwidth if transfer per cycle
  32b
  64b
  128b
Memory at 4 GB/s
  Which widths make bus the bottleneck?
  Memory?

## Slide 68: Width
Will transfer at width of data type give
May need to pack and unpack data to exploit full width

## Slide 69: Big Ideas
Data between PS and PL managed as DMA
Can exploit familiar parallelism
  Thread, Data, Streaming Dataflow
  Overlap compute and communicate
Must manage some pieces pretty explicitly

## Slide 70: Admin
Feedback including HW5
Reading for Wednesday on web
HW6
  Due on Friday