## Slide 1: ESE5320: System-on-a-Chip Architecture
Day 14: October 16, 2024
Orchestrating Data in Memories
Midterm Average: 58
Std. Dev.: YY
Will take max(midterm,final) for midterm grade

## Slide 2: Today
DRAM (Part 1)
DRAM Implications (Part 2)
Tricks for working with DRAM and generally minimizing use of large memories
  Data Reuse in Images (Part 3)
  Sort (time permitting) (Part 4)

## Slide 3: Message
How we access data matters
Reuse data to avoid access to large memories
Think about how organize computation and data to minimize
  Use of large memory
  Data movement
…and think about what you expect, so can diagnose unnecessary data bottlenecks

## Slide 4: Day 3: Memory Scaling
Small memories are fast
  Large memories are slow
Small memories low energy
  Large memories high energy
Large memories dense
  Small memories cost more area per bit
Combining:
  Dense memories are slow

## Slide 5: Day 3: Lesson
Cheaper to access wide/contiguous blocks memory
  In hardware
  From the architectures typically build
Can achieve higher bandwidth on large block data transfer
  Than random access of small data items

## Slide 6: DRAM Dynamic Random Access Memory
Usually the largest memory

## Slide 7: Dynamic RAM
Shares even more logic among bits
Share refresh/restoration logic as well
Minimal storage is a capacitor
“Feature” DRAM process is ability to make capacitors efficiently
Denser, but slower

## Slide 8: DRAM
1GB DDR3 SDRAM from Micron
  http://www.micron.com/products/dram/ddr3/
  96 pin pakage
  16b datapath IO
  Operate at 500+MHz
  37.5ns random access latency

## Slide 9: Memory Access Timing
Access:
  Address (RCD)

## Slide 10: Memory Access Timing
Access:
  Address (RCD)
  Row fetch (RP)

## Slide 11: Memory Access Timing
Access:
  Address (RCD)
  Row fetch (RP)
  Column select (CL)

## Slide 12: Memory Access Timing
Access:
  Address (RCD)
  Row fetch (RP)
  Column select (CL)
  writeback/refresh

## Slide 13: Dynamic RAM
Shares even more logic among bits
Share refresh/restoration logic as well
Minimal storage is a capacitor
“Feature” DRAM process is ability to make capacitors efficiently
Denser, but slower

## Slide 14: Memory Access Timing
Access:
  Address (RCD)
  Row fetch (RP)
  Column select (CL)
  writeback/refresh

## Slide 15: Memory Access Timing
Access:
  Address (RCD)
  Row fetch (RP)
  Column select (CL)
  writeback/refresh
Optimization for access within a row

## Slide 16: DRAM
1GB DDR3 SDRAM from Micron
  http://www.micron.com/products/dram/ddr3/
  96 pin pakage
  16b datapath IO
  Operate at 500+MHz
  37.5ns random access latency

## Slide 17: Memory Access Timing
Access
  Address (RCD)
  Row fetch (RP)
  Column select
    CL: Can repeat
  writeback/refresh
Row 1024b—8192b
Faster to access within row

## Slide 18: Preclass 4
Preclass 4 toy warmup
  Reading n 16b words takes: 10+n cycles
    10 cycles for access latency (RCD, RP)
    1 cycle to select each word (CL)
      n cycles for n of them
% time in access latency
  Reading 1 word
  Reading 16 words
  Reading 128 words

## Slide 19: DRAM
1GB DDR3 SDRAM from Micron
  http://www.micron.com/products/dram/ddr3/
  96 pin pakage
  16b datapath IO
  Operate at 500+MHz
  37.5ns random access latency

## Slide 20: DRAM Streaming
Can design to shift out large data from row

## Slide 21: DRAM Streaming
Reading row is 2x12.5ns
  (RCD,RP)
16b @ 500MHz
1024b row
1024/16
  64 words per row
How long (ns) to provide full row (64, 16b words) from address?

## Slide 22: DRAM Streaming
Can read from wide memory, but only have 16 pins to bring off chip
But, can clock across those 16 pins at high clock rate compared to memory reference (2ns vs. 12.5ns)
So, can sequentially shift the data out the 16 pins, if grabbing all the data for the row

## Slide 23: DRAM
1GB DDR3 SDRAM from Micron
  http://www.micron.com/products/dram/ddr3/
  96 pin pakage
  16b datapath IO
  Operate at 500+MHz
  37.5ns random access latency

## Slide 24: 1 Gigabit DDR2 SDRAM
[Source: http://www.elpida.com/en/news/2004/11-18.html]

## Slide 25: DIMMS multi-DRAM
DIMMs usually pack multiple DRAM chips, c, in parallel
  Can access c*16b per transfer
  Typically 64, 128, 256b wide
    8 chips = 128b wide
https://commons.wikimedia.org/wiki/File:DIMMs.jpg

## Slide 26: Smart Phone
Will use single DRAM chip
iPhone/iPod – flip chip in package with SoC Processor
Apple APL1W72 A11 Bionic SoC layered over SK Hynix H9HKNNNDBMAUUR 3 GB LPDDR4x RAM
Source:
https://www.ifixit.com/Teardown/iPhone+X+Teardown/98975

## Slide 27: Xilinx/Vitis DMA?
This section focused on what the DRAM can do
  What should happen with an optimized DRAM controller
  Only DRAM is contributing latency

## Slide 28: Xilinx AXI Connection to DRAM
Additional Latency from on-chip interconnect and interface
Source: https://www.xilinx.com/html_docs/xilinx2020_1/vitis_doc/programmingvitishls.html

## Slide 29: Xilinx/Vitis DMA?
This section focused on what the DRAM can do
  What should happen with an optimized DRAM controller
Vitis DMA requires setup time
  Which will be in addition to DRAM access time
  High overhead [as you will see on HW6]
    Even higher premium for large block transfers

## Slide 30: DRAM Implications
Part 2

## Slide 31: Terminology Watch
Need to talk about
  DRAM Rows
  Image Rows
  Relation between DRAM and Image Rows

## Slide 32: Preclass 1
How many cycles to run loop?
  10 cycle on dram row change (RCD,RP,CL)
  3 cycles same row (CL)
  128 uint16_b per DRAM row (2048b)

## Slide 33: Image Row and DRAM Rows
Address | MSB -- DRAM Row Bytes -- LSB |  |  |  |  |  |  | 
0x027FF0 | [y-1,1023] |  |  |  |  |  |  | 
0x028000 | [y,127] |  |  |  |  |  |  | [y,0]
0x028100 |  |  |  |  |  |  |  | [y,128]
0x028200 |  |  |  |  |  |  |  | 
0x028300 |  |  |  |  |  |  |  | 
0x028400 |  |  |  |  |  |  |  | 
0x028500 |  |  |  |  |  |  |  | 
0x028600 |  |  |  |  |  |  |  | 
0x028700 | [y,1023] |  |  |  |  |  |  | [y,896]
0x028800 |  |  |  |  |  |  |  | [y+1,0]
0x028900 |  |  |  |  |  |  |  | 
0x028a00 |  |  |  |  |  |  |  | 

## Slide 34: Preclass 2
How many cycles to run loop?
  10 cycle on row change
  3 cycles same row
  128 uint16_b per DRAM row (2048b)
Note loop
interchange

## Slide 35: Preclass 3
How many cycles to run loop?
  10+n cycles to fetch n<=128 Half-words on row

## Slide 36: DRAM
Latency is large (10s of ns)
Throughput can be high (GB/s)
  If accessed sequentially
  If exploit wide-word block transfers
Throughput low on random accesses
  As we saw for random access on wide-word memory
Integer factor – order of magnitude -- difference

## Slide 37: Day 13: Data Movement (Options)
DMA burst copy into BRAM memories
  Built on top of other with DMA copy loop

## Slide 38: Maximize Reuse Part 3
Minimize need to go to large memory

## Slide 39: Data Management
Large, central memory
  Bottleneck
  High energy
Minimize need to return to it

## Slide 40: Window Filter
Compute based on neighbors
  F(d[y-1][x-1],d[y-1][x],d[y-1][x+1], d[y][x-1],d[y][x],d[y][x+1], d[y+1][x-1],d[y+1][x],d[y+1][x+1])
Common idiom
  Image filtering
  CNN (Convolution stage in Deep Neural Network)
  Numerical simulation
  Cellular automata
  Search, matching

## Slide 41: Window Filter
Compute based on neighbors
  F(d[y-1][x-1],d[y-1][x],d[y-1][x+1], d[y][x-1],d[y][x],d[y][x+1], d[y+1][x-1],d[y+1][x],d[y+1][x+1])
Generalize for different neighborhood sizes
  for (yoff=YMIN; yoff<YMAX;yoff++) for (xoff=XMIN; xoff<XMAX;xoff++) res=fun(res,d[y+yoff][x+xoff]);

## Slide 42: Window Filter
Compute based on neighbors
for (y=0;y<YMAX;y++) for (x=0;x<XMAX;x++)
  o[y][x]=F(d[y-1][x-1],d[y-1][x],d[y-1][x+1], d[y][x-1],d[y][x],d[y][x+1], d[y+1][x-1],d[y+1][x],d[y+1][x+1]);
How work with image in DRAM
  As written references
  Reads per row?

## Slide 43: Window Filter
Compute based on neighbors
for (y=0;y<YMAX;y++) for (x=0;x<XMAX;x++)
  o[y][x]=F(d[y-1][x-1],d[y-1][x],d[y-1][x+1], d[y][x-1],d[y][x],d[y][x+1], d[y+1][x-1],d[y+1][x],d[y+1][x+1]);
Data reused between inner loop invocations when x increments?
  How many of the 9 values are reused at x+1?

## Slide 44: Window Shift x++
 | 23 | 24 | 25 | 26 | 27
17 |  |  |  |  | 
18 |  | Y-1,X-1 | Y-1,X | Y-1,X+1 | 
19 |  | Y,X-1 | Y,X | Y,X+1 | 
20 |  | Y+1,X-1 | Y+1,X | Y+1,X+1 | 
21 |  |  |  |  | 
 | 23 | 24 | 25 | 26 | 27
17 |  |  |  |  | 
18 |  |  | Y-1,X-1 | Y-1,X | Y-1,X+1
19 |  |  | Y,X-1 | Y,X | Y,X+1
20 |  |  | Y+1,X-1 | Y+1,X | Y+1,X+1
21 |  |  |  |  | 

## Slide 45: Window Filter
Compute based on neighbors
for (y=0;y<YMAX;y++) for (x=0;x<XMAX;x++)
  o[y][x]=F(d[y-1][x-1],d[y-1][x],d[y-1][x+1], d[y][x-1],d[y][x],d[y][x+1], d[y+1][x-1],d[y+1][x],d[y+1][x+1]);
Data reused between y values in outer loop?
  How many of 9 values reused for y+1?

## Slide 46: Window Shift y++
 | 23 | 24 | 25 | 26 | 27
17 |  |  |  |  | 
18 |  | Y-1,X-1 | Y-1,X | Y-1,X+1 | 
19 |  | Y,X-1 | Y,X | Y,X+1 | 
20 |  | Y+1,X-1 | Y+1,X | Y+1,X+1 | 
21 |  |  |  |  | 
 | 23 | 24 | 25 | 26 | 27
17 |  |  |  |  | 
18 |  |  |  |  | 
19 |  | Y-1,X-1 | Y-1,X | Y-1,X+1 | 
20 |  | Y,X-1 | Y,X | Y,X+1 | 
21 |  | Y+1,X-1 | Y+1,X | Y+1,X+1 | 

## Slide 47: Window Filter
Compute based on neighbors
for (y=0;y<YMAX;y++) for (x=0;x<XMAX;x++)
  o[y][x]=F(d[y-1][x-1],d[y-1][x],d[y-1][x+1], d[y][x-1],d[y][x],d[y][x+1], d[y+1][x-1],d[y+1][x],d[y+1][x+1]);
Data reused between y values in outer loop?
  How many of 9 values reused for y+1?
  Reuse distance [in cycles]?
    …assume II=1 pipeline inner loop
    i.e. how many o[y][x]’s do we compute between using as d[y+1][x] and d[y][x] ?

## Slide 48: Window Filter
Compute based on neighbors
for (y=0;y<YMAX;y++) for (x=0;x<XMAX;x++)
  o[y][x]=F(d[y-1][x-1],d[y-1][x],d[y-1][x+1], d[y][x-1],d[y][x],d[y][x+1], d[y+1][x-1],d[y+1][x],d[y+1][x+1]);
How much data need to store to hold on to d[y] values that will use again?
Where can we store?

## Slide 49: Line Buffers
Only need to save last 2 rows (d[y][*])
  General case: (window_height-1) rows
Store in local buffers
  Call them dy[XMAX], dym[XMAX];
    dym for dy minus 1
  Stick value there between uses.

## Slide 50: Variable Naming
 |  | +xm |  | +xp | 
dym |  | Y-1,X-1 | Y-1,X | Y-1,X+1 | 
dy |  | Y,X-1 | Y,X | Y,X+1 | 
dyp |  | Y+1,X-1 | Y+1,X | Y+1,X+1 | 
 |  | +xm |  | +xp | 
dym |  | Y-1,X-1 | Y-1,X | Y-1,X+1 | 
dy |  | Y,X-1 | Y,X | Y,X+1 | 
dyp |  | dypxm | dypx | dnew | 

## Slide 51: Window Filter
With line buffers dy, dym
for (y=0;y<YMAX;y++) for (x=0;x<XMAX;x++) {
  dypxm=dypx; dypx=dnew; dnew=d[y+1][x+1];
  o[y][x]=F(dym[x-1],dym[x],dym[x+1], dy[x-1],dy[x],dy[x+1], dypxm,dypx,dnew);
  dym[x-1]=dy[x-1];
  dy[x-1]=dypxm;
  }

## Slide 52: Lines in Buffers
 |  | +xm |  | +xp | 
dym |  | Y-1,X-1 | Y-1,X | Y-1,X+1 | 
dy |  | Y,X-1 | Y,X | Y,X+1 | 
dyp |  | Y+1,X-1 | Y+1,X | Y+1,X+1 | 

## Slide 53: Window Filter
With line buffers dy, dym
for (y=0;y<YMAX;y++) for (x=0;x<XMAX;x++) {
  dypxm=dypx; dypx=dnew; dnew=d[y+1][x+1];
  o[y][x]=F(dym[x-1],dym[x],dym[x+1], dy[x-1],dy[x],dy[x+1], dypxm,dypx,dnew);
  dym[x-1]=dy[x-1];dy[x-1]=dypxm; }
Avoid multiple read dy, dym?
  Save memory ports

## Slide 54: Variable Naming
 |  | +xm |  | +xp | 
dym |  | Y-1,X-1 | Y-1,X | Y-1,X+1 | 
dy |  | Y,X-1 | Y,X | Y,X+1 | 
dyp |  | Y+1,X-1 | Y+1,X | Y+1,X+1 | 
 |  | +xm |  | +xp | 
dym |  | dymxm | dymx | dymxp | 
dy |  | dyxm | dyx | dyxp | 
dyp |  | dypxm | dypx | dnew | 

## Slide 55: Window Filter
Single read and write from dym, dy
for (y=0;y<YMAX;y++) for (x=0;x<XMAX;x++) {
  dypxm=dypx; dypx=dnew; dnew=d[y+1][x+1];
  dyxm=dyx; dyx=dyxp; dyxp=dy[x+1];
  dymxm=dymx; dymx=dymxp; dymxp=dym[x+1];
  o[y][x]=F(dymxm,dymx,dymxp, dyxm,dyx,dyxp, dypxm,dypx,dnew);
  dym[x-1]=dyxm;dy[x-1]=dypxm; }

## Slide 56: Pipelined Circuit
Single sequential read from big memory (DRAM) per result
Shift registers
Line buffers

## Slide 57: Window Filter
Convert to stream … use Preclass 3 load
for (y=0;y<YMAX;y++) for (x=0;x<XMAX;x++) {
  dypxm=dypx; dypx=dnew; astream.read(dnew);
  dyxm=dyx; dyx=dyxp; dyxp=dy[x+1];
  dymxm=dymx; dymx=dymxp; dymxp=dym[x+1];
  o[y][x]=F(dymxm,dymx,dymxp, dyxm,dyx,dyxp, dypxm,dypx,dnew);
  dym[x-1]=dyxm;dy[x-1]=dypxm; }

## Slide 58: Window Filter
Convert to stream … use Preclass 3 load
for (y=0;y<YMAX;y++) for (x=0;x<XMAX;x++) {
  dypxm=dypx; dypx=dnew; astream.read(dnew);
  dyxm=dyx; dyx=dyxp; dyxp=dy[x+1];
  dymxm=dymx; dymx=dymxp; dymxp=dym[x+1];
  ostream.write(F(dymxm,dymx,dymxp, dyxm,dyx,dyxp, dypxm,dypx,dnew));
  dym[x-1]=dyxm;dy[x-1]=dypxm; }

## Slide 59: Multiple Filters
What if want to run multiple filters?
for (f=0;f<FMAX;f++) for (y=0;y<YMAX;y++) for (x=0;x<XMAX;x++)
  o[f][y][x]=fun[f](d[y-1][x-1],d[y-1][x],d[y-1][x+1], d[y][x-1],d[y][x],d[y][x+1], d[y+1][x-1],d[y+1][x],d[y+1][x+1]);
Forces multiple reads through d
Avoidable?

## Slide 60: Take-Away
Can process with a single, streaming read through data in large memory
  Specifically for window filters on images
  General goal to try to achieve
Careful to orchestrate data in small, local buffers
DMA/streaming transfers to achieve near peak DRAM bandwidth

## Slide 61: Sort Part 4
Cover in lecture session if time permits
Skip to wrapup

## Slide 62: Sort
Order data
  7 3 4 2 1 9 8 0  0 1 2 3 4 7 8 9
Data movement can be challenging
  Last value may become first (vice-versa)
  Especially when not fit in small memories
Many sequential sort solutions access data irregularly
  Want to avoid with DRAM
Example illustrates can reformulate as streaming

## Slide 63: Observation: Merge
Merging two sorted list is a streaming operation
int aptr; int bptr;
for (i=0;i<MCNT;i++)
  If ((aptr<ACNT) && (bptr<BCNT))
  If (a[aptr]>b[bptr])
  { o[i]=a[aptr]; aptr++; }
  Else
  { o[i]=b[bptr]; bptr++; }
  Else // copy over remaining from a or b

## Slide 64: Merge Memory Access
for (i=0;i<MCNT;i++)
  If ((aptr<ACNT) && (bptr<BCNT))
  If (a[aptr]>b[bptr])
  { o[i]=a[aptr]; aptr++; }
  Else
  { o[i]=b[bptr]; bptr++; }
  Else // copy over remaining from a or b
How work with DRAM rows?

## Slide 65: Merge and DRAM
May alternate between DRAM rows
Int aptr; int bptr;
For (i=0;i<MCNT;i++)
  If ((aptr<ACNT) && (bptr<BCNT))
  If (a[aptr]>b[bptr])
  { o[i]=a[aptr]; aptr++; }
  Else
  { o[i]=b[bptr]; bptr++; }
  Else // copy over remaining from a or b

## Slide 66: Merge and DRAM
Want to fetch a as block into local memory (into stream), then can do this
Int aptr; int bptr;
For (i=0;i<MCNT;i++)
  If ((aptr<ACNT) && (bptr<BCNT))
  If (a[aptr]>b[bptr])
  { o[i]=a[aptr]; aptr++; }
  Else
  { o[i]=b[bptr]; bptr++; }
  Else // copy over remaining from a or b

## Slide 67: Merge using Streams
Merging two sorted list is a streaming operation
int aptr; int bptr;
astream.read(ain); bstream.read(bin)
for (i=0;i<MCNT;i++)
  If ((aptr<ACNT) && (bptr<BCNT))
  If (ain>bin)
  { ostream.write(ain); aptr++; astream.read(ain);}
  Else
  { ostream.write(bin) bptr++; bstream.read(bin);}
  Else // copy over remaining from astream/bstream

## Slide 68: Merge using Streams and DRAM
Streaming accomplishes if Streaming is implemented to fetch row into FIFO buffer
Int ptr; int bptr;
astream.read(ain); bstream.read(bin)
For (i=0;i<MCNT;i++)
  If ((aptr<ACNT) && (bptr<BCNT))
  If (ain>bin)
  { ostream.write(ain); aptr++; astream.read(ain);}
  Else
  { ostream.write(bin) bptr++; bstream.read(bin);}
  Else // copy over remaining from astream/bstream

## Slide 69: Building from Merge
Know how to get sorted data of length N given two, independently sorted lists of length N/2
A list of length 1 is sorted.
Merging two lists of length 1 gives us?
  How many lists of what length?
Merging two lists of length 2 gives us?

## Slide 70: Merge Sort
Strategy
  For i=1 to passes
    Pass over data creating merged sequences of length 2i from pairs of length 2i-1
  What is passes?
Can, at least, limit to passes reads through data from large memory.

## Slide 71: On-chip Merge
As long as can fit sequence (2i) on chip, can stream merge stages without going back to big memory (DRAM)
merge
alternate
2i-1
2i
2i

## Slide 72: On-chip Merge
As long as can fit sequence (2i) on chip, can stream merge stages without going back to big memory (DRAM)
  E.g. with 36Kb BRAMs ~ first 10-12 stages
    Up to ~16 using multiple BRAMs
merge+alt
merge+alt
merge+alt

## Slide 73: On-chip Merge
For sorts up to ~100K elements may be able to cover in one read/write stream to/from DRAM
Larger: ~log2(N)-15 read/writes
merge+alt
merge+alt
merge+alt

## Slide 74: Big Ideas
Must pay attention to orchestrate data movement
  How we access and reuse data
Minimize use of large memories
Regular (sequential) access to large memories higher performance
  Easier to get bandwidth on wide-word reads

## Slide 75: Admin
Feedback
HW6 due Friday
Reading for Monday on web
HW7: out