## Slide 1: ESE5320: System-on-a-Chip Architecture
Day 17: Oct. 28, 2024
LZW, Associative Maps

## Slide 2: Today
LZW Compression Algorithm (Part 1)
Associative Memory
  Custom (part 2)
  FPGA (Part 3, time permitting)

## Slide 3: Message
Can adaptively compress data using recurring substrings
Rich design space for Maps

## Slide 4: Idea
Use data already sent as the dictionary
  Give short names to things in dictionary
  Don’t need to pre-arrange dictionary
  Adapt to common phrases/idioms in a particular document

## Slide 5: Encoding
Greedy simplification
  Encode by successively selecting the longest match between the head of the remaining string to send and the current window

## Slide 6: Algorithm Concept
While data to send
  Find largest match in window of data sent
  If length too small (length=1)
    Send character
  Else
    Send <x,y> = <match-pos,length>
  Add data encoded into sent window

## Slide 7: Part 1: LZW Compression Lempel-Ziv-Welch

## Slide 8: Idea
Avoid O(Dictionary-size) work
  Only need to match against positions that start with the character(s) in string to encode
    Separate dictionary for each?
Only check position 0 for “starts with I”

## Slide 9: Idea
Avoid O(Dictionary-size) work
  Only need to match against positions that start with the character(s) in string to encode
    Separate dictionary for each?
T-dictionary:
  Tap, The, Their, Then, There, Tuesday

## Slide 10: Idea
Avoid O(Dictionary-size) work
  Only need to match against positions that start with the character(s) in string to encode
    Separate dictionary for each?
T-dictionary:
  Tap, The, Their, Then, There, Tuesday
If prefix same, why check redundantly?
  Generalize: Store things with common prefix together
    Share prefix among substrings
  Represent all strings as prefix tree

## Slide 11: Idea
Avoid O(Dictionary-size) work
  Only need to match against positions that start with the character(s) in string to encode
    Separate dictionary for each?
If prefix same, why check redundantly?
  Store things with common prefix together
  Share prefix among substrings
  Represent all strings as prefix tree
Follow prefix trees with fixed work per input character

## Slide 12: Tree Algorithm
Tree Root for each character
Follow tree according to input until no more match
Send <name of last tree node>
  Dictionary entry
    Named sequentially by insertion
Extend tree (dictionary) with new character
Start over with this character

## Slide 13: I AM SAM SAM I AM
Input | Send | Dict | Add Entry | Add What
I | <nothing> |  |  | 

## Slide 14: I AM SAM SAM I AM
Input | Send | Dict | Add Entry | Add What
I | <nothing> |  |  | 
 | ??? | I | ??? | ???

## Slide 15
Note: the “Add What” arrows are shown
  the way we would backtrack to recover the string
  rather than the way trace forward for matching
  (may change for lecture)

## Slide 16: I AM SAM SAM I AM
Input | Send | Dict | Add Entry | Add What
I | <nothing> |  |  | 
 | 73 | I | 256 | I<-spc
256
I
<spc>

## Slide 17: I AM SAM SAM I AM
Input | Send | Dict | Add Entry | Add What
I | <nothing> |  |  | 
 | 73 | I | 256 | I<-spc
A | ??? | spc | ??? | ???
256
I
<spc>

## Slide 18: I AM SAM SAM I AM
Input | Send | Dict | Add Entry | Add What
I | <nothing> |  |  | 
 | 73 | I | 256 | I<-spc
A | 32 | spc | 257 | spc<-A
256
I
<spc>
257
<spc>
A

## Slide 19: I AM SAM SAM I AM
Input | Send | Dict | Add Entry | Add What
I | <nothing> |  |  | 
 | 73 | I | 256 | I<-spc
A | 32 | spc | 257 | spc<-A
M | ?? | A | ??? | ???
256
I
<spc>
257
<spc>
A

## Slide 20: I AM SAM SAM I AM
Input | Send | Dict | Add Entry | Add What
I | <nothing> |  |  | 
 | 73 | I | 256 | I<-spc
A | 32 | spc | 257 | spc<-A
M | 65 | A | 258 | A<-M
256
I
<spc>
257
<spc>
A
258
A
M

## Slide 21: I AM SAM SAM I AM
Input | Send | Dict | Add Entry | Add What
I | <nothing> |  |  | 
 | 73 | I | 256 | I<-spc
A | 32 | spc | 257 | spc<-A
M | 65 | A | 258 | A<-M
 | ??? | M | ??? | ???
256
I
<spc>
257
<spc>
A
258
A
M

## Slide 22: I AM SAM SAM I AM
Input | Send | Dict | Add Entry | Add What
I | <nothing> |  |  | 
 | 73 | I | 256 | I<-spc
A | 32 | spc | 257 | spc<-A
M | 65 | A | 258 | A<-M
 | 77 | M | 259 | M<-spc
256
I
<spc>
257
<spc>
A
258
A
M
259
M
<spc>

## Slide 23: I AM SAM SAM I AM
Input | Send | Dict | Add Entry | Add What
I | <nothing> |  |  | 
 | 73 | I | 256 | I<-spc
A | 32 | spc | 257 | spc<-A
M | 65 | A | 258 | A<-M
 | 77 | M | 259 | M<-spc
S | ??? | spc | ??? | ???
256
I
<spc>
257
<spc>
A
258
A
M
260
M
<spc>

## Slide 24: I AM SAM SAM I AM
Input | Send | Dict | Add Entry | Add What
I | <nothing> |  |  | 
 | 73 | I | 256 | I<-spc
A | 32 | spc | 257 | spc<-A
M | 65 | A | 258 | A<-M
 | 77 | M | 259 | M<-spc
S | 32 | spc | 260 | spc<-S
256
I
<spc>
258
A
M
259
M
<spc>
257
<spc>
A
260
S

## Slide 25: I AM SAM SAM I AM
Input | Send | Dict | Add Entry | Add What
I | <nothing> |  |  | 
 | 73 | I | 256 | I<-spc
A | 32 | spc | 257 | spc<-A
M | 65 | A | 258 | A<-M
 | 77 | M | 259 | M<-spc
S | 32 | spc | 260 | spc<-S
A | ??? | S | ??? | ???
256
I
<spc>
258
A
M
259
M
<spc>
257
<spc>
A
260
S

## Slide 26: I AM SAM SAM I AM
Input | Send | Dict | Add Entry | Add What
I | <nothing> |  |  | 
 | 73 | I | 256 | I<-spc
A | 32 | spc | 257 | spc<-A
M | 65 | A | 258 | A<-M
 | 77 | M | 259 | M<-spc
S | 32 | spc | 260 | spc<-S
A | 83 | S | 261 | S<-A
256
I
<spc>
258
A
M
259
M
<spc>
257
<spc>
A
260
S
261
S
A

## Slide 27: I AM SAM SAM I AM
Input | Send | Dict | Add Entry | Add What
I | <nothing> |  |  | 
 | 73 | I | 256 | I<-spc
A | 32 | spc | 257 | spc<-A
M | 65 | A | 258 | A<-M
 | 77 | M | 259 | M<-spc
S | 32 | spc | 260 | spc<-S
A | 83 | S | 261 | S<-A
M | ??? (different) | A | ??? | ???
256
I
<spc>
258
A
M
259
M
<spc>
257
<spc>
A
260
S
261
S
A

## Slide 28: I AM SAM SAM I AM
Input | Send | Dict | Add Entry | Add What
I | <nothing> |  |  | 
 | 73 | I | 256 | I<-spc
A | 32 | spc | 257 | spc<-A
M | 65 | A | 258 | A<-M
 | 77 | M | 259 | M<-spc
S | 32 | spc | 260 | spc<-S
A | 83 | S | 261 | S<-A
M | <nothing> | A |  | 
256
I
<spc>
258
A
M
259
M
<spc>
257
<spc>
A
260
S
261
S
A

## Slide 29: I AM SAM SAM I AM
Input | Send | Dict | Add Entry | Add What
I | <nothing> |  |  | 
 | 73 | I | 256 | I<-spc
A | 32 | spc | 257 | spc<-A
M | 65 | A | 258 | A<-M
 | 77 | M | 259 | M<-spc
S | 32 | spc | 260 | spc<-S
A | 83 | S | 261 | S<-A
M | <nothing> | A |  | 
 | ??? | AM (258) | ??? | ???
256
I
<spc>
258
A
M
259
M
<spc>
257
<spc>
A
260
S
261
S
A

## Slide 30: I AM SAM SAM I AM
Input | Send | Dict | Add Entry | Add What
I | <nothing> |  |  | 
 | 73 | I | 256 | I<-spc
A | 32 | spc | 257 | spc<-A
M | 65 | A | 258 | A<-M
 | 77 | M | 259 | M<-spc
S | 32 | spc | 260 | spc<-S
A | 83 | S | 261 | S<-A
M | <nothing> | A |  | 
 | 258 | AM (258) | 262 | 258<-spc
256
I
<spc>
258
A
M
259
M
<spc>
257
<spc>
A
260
S
261
S
A

## Slide 31: I AM SAM SAM I AM
Input | Send | Dict | Add Entry | Add What
I | <nothing> |  |  | 
 | 73 | I | 256 | I<-spc
A | 32 | spc | 257 | spc<-A
M | 65 | A | 258 | A<-M
 | 77 | M | 259 | M<-spc
S | 32 | spc | 260 | spc<-S
A | 83 | S | 261 | S<-A
M | <nothing> | A |  | 
 | 258 | AM (258) | 262 | 258<-spc
256
I
<spc>
259
M
<spc>
257
<spc>
A
260
S
261
S
A
258
A
M
262
<spc>

## Slide 32: I AM SAM SAM I AM
Input | Send | Dict | Add Entry | Add What
I | <nothing> |  |  | 
 | 73 | I | 256 | I<-spc
A | 32 | spc | 257 | spc<-A
M | 65 | A | 258 | A<-M
 | 77 | M | 259 | M<-spc
S | 32 | spc | 260 | spc<-S
A | 83 | S | 261 | S<-A
M | <nothing> | A |  | 
 | 258 | AM | 262 | 258<-spc
S | ??? | spc | ??? | ???
256
I
<spc>
259
M
<spc>
257
<spc>
A
260
S
261
S
A
258
A
M
262
<spc>

## Slide 33: I AM SAM SAM I AM
Input | Send | Dict | Add Entry | Add What
I | <nothing> |  |  | 
 | 73 | I | 256 | I<-spc
A | 32 | spc | 257 | spc<-A
M | 65 | A | 258 | A<-M
 | 77 | M | 259 | M<-spc
S | 32 | spc | 260 | spc<-S
A | 83 | S | 261 | S<-A
M | <nothing> | A |  | 
 | 258 | AM (258) | 262 | 258<-spc
S | <nothing> | spc |  | 
256
I
<spc>
259
M
<spc>
257
<spc>
A
260
S
261
S
A
258
A
M
262
<spc>

## Slide 34: I AM SAM SAM I AM
Input | Send | Dict | Add Entry | Add What
I | <nothing> |  |  | 
 | 73 | I | 256 | I<-spc
A | 32 | spc | 257 | spc<-A
M | 65 | A | 258 | A<-M
 | 77 | M | 259 | M<-spc
S | 32 | spc | 260 | spc<-S
A | 83 | S | 261 | S<-A
M | <nothing> | A |  | 
 | 258 | AM | 262 | 258<-spc
S | <nothing> | spc |  | 
A | ??? | spc S (260) | ??? | ???
256
I
<spc>
259
M
<spc>
257
<spc>
A
260
S
261
S
A
258
A
M
262
<spc>

## Slide 35: I AM SAM SAM I AM
Input | Send | Dict | Add Entry | Add What
I | <nothing> |  |  | 
 | 73 | I | 256 | I<-spc
A | 32 | spc | 257 | spc<-A
M | 65 | A | 258 | A<-M
 | 77 | M | 259 | M<-spc
S | 32 | spc | 260 | spc<-S
A | 83 | S | 261 | S<-A
M | <nothing> | A |  | 
 | 258 | AM | 262 | 258<-spc
S | <nothing> | spc |  | 
A | 260 | spc S | 263 | 260<-A
256
I
<spc>
259
M
<spc>
261
S
A
258
A
M
262
<spc>
257
<spc>
A
260
S
263
A

## Slide 36: I AM SAM SAM I AM
Input | Send | Dict | Add Entry | Add What
I | <nothing> |  |  | 
 | 73 | I | 256 | I<-spc
A | 32 | spc | 257 | spc<-A
M | 65 | A | 258 | A<-M
 | 77 | M | 259 | M<-spc
S | 32 | spc | 260 | spc<-S
A | 83 | S | 261 | S<-A
M | <nothing> | A |  | 
 | 258 | AM | 262 | 258<-spc
S | <nothing> | spc |  | 
A | 260 | spc S | 263 | 260<-A
M | ??? | A | ??? | ???
256
I
<spc>
259
M
<spc>
261
S
A
258
A
M
262
<spc>
257
<spc>
A
260
S
263
A

## Slide 37: I AM SAM SAM I AM
Input | Send | Dict | Add Entry | Add What
I | <nothing> |  |  | 
 | 73 | I | 256 | I<-spc
A | 32 | spc | 257 | spc<-A
M | 65 | A | 258 | A<-M
 | 77 | M | 259 | M<-spc
S | 32 | spc | 260 | spc<-S
A | 83 | S | 261 | S<-A
M | <nothing> | A |  | 
 | 258 | AM (258) | 262 | 258<-spc
S | <nothing> | spc |  | 
A | 260 | spc S (260) | 263 | 260<-A
M | <nothing> | A |  | 
256
I
<spc>
259
M
<spc>
261
S
A
258
A
M
262
<spc>
257
<spc>
A
260
S
263
A

## Slide 38: I AM SAM SAM I AM
Input | Send | Dict | Add Entry | Add What
I | <nothing> |  |  | 
 | 73 | I | 256 | I<-spc
A | 32 | spc | 257 | spc<-A
M | 65 | A | 258 | A<-M
 | 77 | M | 259 | M<-spc
S | 32 | spc | 260 | spc<-S
A | 83 | S | 261 | S<-A
M | <nothing> | A |  | 
 | 258 | AM (258) | 262 | 258<-spc
S | <nothing> | spc |  | 
A | 260 | spc S (260) | 263 | 260<-A
M | <nothing> | A |  | 
 | ??? | AM (258) | ??? | ???
256
I
<spc>
259
M
<spc>
261
S
A
258
A
M
262
<spc>
257
<spc>
A
260
S
263
A

## Slide 39: I AM SAM SAM I AM
Input | Send | Dict | Add Entry | Add What
I | <nothing> |  |  | 
 | 73 | I | 256 | I<-spc
A | 32 | spc | 257 | spc<-A
M | 65 | A | 258 | A<-M
 | 77 | M | 259 | M<-spc
S | 32 | spc | 260 | spc<-S
A | 83 | S | 261 | S<-A
M | <nothing> | A |  | 
 | 258 | AM (258) | 262 | 258<-spc
S | <nothing> | spc |  | 
A | 260 | spc S (260) | 263 | 260<-A
M | <nothing> | A |  | 
 | <nothing> | AM (252) |  | 
256
I
<spc>
259
M
<spc>
261
S
A
258
A
M
262
<spc>
257
<spc>
A
260
S
263
A

## Slide 40: I AM SAM SAM I AM
Input | Send | Dict | Add Entry | Add What
I | <nothing> |  |  | 
 | 73 | I | 256 | I<-spc
A | 32 | spc | 257 | spc<-A
M | 65 | A | 258 | A<-M
 | 77 | M | 259 | M<-spc
S | 32 | spc | 260 | spc<-S
A | 83 | S | 261 | S<-A
M | <nothing> |  |  | 
 | 258 | AM (258) | 262 | 258<-spc
S | <nothing> |  |  | 
A | 260 | spc S (260) | 263 | 260<-A
M | <nothing> | A |  | 
 | <nothing> | AM (258) |  | 
I | ??? | AM spc (262) | ??? | ???
256
I
<spc>
259
M
<spc>
261
S
A
258
A
M
262
<spc>
257
<spc>
A
260
S
263
A

## Slide 41: I AM SAM SAM I AM
Input | Send | Dict | Add Entry | Add What
I | <nothing> |  |  | 
 | 73 | I | 256 | I<-spc
A | 32 | spc | 257 | spc<-A
M | 65 | A | 258 | A<-M
 | 77 | M | 259 | M<-spc
S | 32 | spc | 260 | spc<-S
A | 83 | S | 261 | S<-A
M | <nothing> |  |  | 
 | 258 | AM (258) | 262 | 258<-spc
S | <nothing> |  |  | 
A | 260 | spc S (260) | 263 | 260<-A
M | <nothing> | A |  | 
 | <nothing> | AM (258) |  | 
I | 262 | AM spc (262) | 264 | 262<-I
256
I
<spc>
259
M
<spc>
261
S
A
258
A
M
262
<spc>
257
<spc>
A
260
S
263
A

## Slide 42: I AM SAM SAM I AM
Input | Send | Dict | Add Entry | Add What
I | <nothing> |  |  | 
 | 73 | I | 256 | I<-spc
A | 32 | spc | 257 | spc<-A
M | 65 | A | 258 | A<-M
 | 77 | M | 259 | M<-spc
S | 32 | spc | 260 | spc<-S
A | 83 | S | 261 | S<-A
M | <nothing> |  |  | 
 | 258 | AM (258) | 262 | 258<-spc
S | <nothing> |  |  | 
A | 260 | spc S (260) | 263 | 260<-A
M | <nothing> | A |  | 
 | <nothing> | AM (258) |  | 
I | 262 | AM spc (262) | 264 | 262<-I
256
I
<spc>
259
M
<spc>
261
S
A
258
A
M
262
<spc>
257
<spc>
A
260
S
263
A
264
I

## Slide 43: Large Memory Implementation
int encode[SIZE][256];
Name tree node by insertion order
c is a character
Encode[x][c] holds the next tree node that extends tree node x by symbol c
  Or NONE if there is no such tree node

## Slide 44: Memory Tree Algorithm
curr=0; // pointer into input chunk
nextdict=NUM_SYMBOLS;
// dict[i]= symbol i for i<NUM_SYMBOLS
while (curr<chunk_size)
while(encode[x][input[curr]]!=NONE)
x=encode[x][input[curr]]; curr++;
send x
tree[nextdict].parent=x;
tree[nextdict].sym=input[curr];
encode[x][input[curr]]=nextdict++;
x=input[curr]; curr++;

## Slide 45: Memory Tree Algorithm
curr=0; // pointer into input chunk
nextdict=NUM_SYMBOLS;
// dict[i]= symbol i for i<NUM_SYMBOLS
while (curr<chunk_size)
while(encode[x][input[curr]]!=NONE)
x=encode[x][input[curr]]; curr++;
send x
tree[nextdict].parent=x;
tree[nextdict].sym=input[curr];
encode[x][input[curr]]=nextdict++;
x=input[curr]; curr++;
Follow
Tree

## Slide 46: Memory Tree Algorithm
curr=0; // pointer into input chunk
nextdict=NUM_SYMBOLS;
// dict[i]= symbol i for i<NUM_SYMBOLS
while (curr<chunk_size)
while(encode[x][input[curr]]!=NONE)
x=encode[x][input[curr]]; curr++;
send x
tree[nextdict].parent=x;
tree[nextdict].sym=input[curr];
encode[x][input[curr]]=nextdict++;
x=input[curr]; curr++;
258
A
M
262
264
I
<spc>

## Slide 47: I AM SAM SAM I AM
Input | Send | Dict | Add Entry | Add What
I | <nothing> |  |  | 
 | 73 | I | 256 | I<-spc
A | 32 | spc | 257 | spc<-A
M | 65 | A | 258 | A<-M
 | 77 | M | 259 | M<-spc
S | 32 | spc | 260 | spc<-S
A | 83 | S | 261 | S<-A
M | <nothing> |  |  | 
 | 258 | AM (258) | 262 | 258<-spc
S | <nothing> |  |  | 
A | 260 | spc S (260) | 263 | 260<-A
M | <nothing> | A |  | 
 | <nothing> | AM (258) |  | 
I | 262 | AM spc (262) | 264 | 262<-I
256
I
<spc>
259
M
<spc>
261
S
A
258
A
M
262
<spc>
257
<spc>
A
260
S
263
A
264
I

## Slide 48: Memory Tree Algorithm
curr=0; // pointer into input chunk
nextdict=NUM_SYMBOLS;
// dict[i]= symbol i for i<NUM_SYMBOLS
while (curr<chunk_size)
while(encode[x][input[curr]]!=NONE)
x=encode[x][input[curr]]; curr++;
send x
tree[nextdict].parent=x;
tree[nextdict].sym=input[curr];
encode[x][input[curr]]=nextdict++;
x=input[curr]; curr++;
How much work per
character to encode?
Hint: between curr++
executions?

## Slide 49: Map
Later today or Wednesday will talk about higher-level maps
Version of encode/decode in
  Geeks-for-Geeks description
  Decoder we provide
Based on Maps of strings
  Simpler to state
  Likely not O(1) per symbol
  More expensive implementation in hardware
    Version here better for hardware (keeps simple)

## Slide 50: Algorithm with Map
curr=0; // pointer into input chunk
nextdict=NUM_SYMBOLS;
// dict initialized symbol i for i<NUM_SYMBOLS
while (curr<chunk_size)
while(dict.lookup(x+input[curr])!=NONE)
x=x+input[curr]; curr++;
send dic.lookup(x);
dict.insert(x+input[curr],nextdict++);
x=String(input[curr]); curr++;

## Slide 51: I AM SAM SAM I AM
Input | Send | Dict | Add Entry | Add What
I | <nothing> |  |  | 
 | 73 | I | 256 | I<-spc
A | 32 | spc | 257 | spc<-A
M | 65 | A | 258 | A<-M
 | 77 | M | 259 | M<-spc
S | 32 | spc | 260 | spc<-S
A | 83 | S | 261 | S<-A
M | <nothing> |  |  | 
 | 258 | AM (258) | 262 | 258<-spc
S | <nothing> |  |  | 
A | 260 | spc S (260) | 263 | 260<-A
M | <nothing> | A |  | 
 | <nothing> | AM (258) |  | 
I | 262 | AM spc (262) | 264 | 262<-I
256
I
<spc>
259
M
<spc>
261
S
A
258
A
M
262
<spc>
257
<spc>
A
260
S
263
A
264
I

## Slide 52: Compact Memory
int encode[SIZE][256];
How many entries in this table are not NONE?
  Maximum number of times execute:
  encode[x][input[curr]]=nextdict++;
  Maximum number of entries added to encode?
  Maximum number of NONE entries in encode?

## Slide 53: Compact Memory
int encode[SIZE][256];
Table is very sparse
If store as associative memory
  At most SIZE entries
    (SIZE+256 with first 256 entries for each byte value)
Look at how to implement associative memories next

## Slide 54: LZW So Far – 4KB chunks
Brute Force
  Needs one byte per byte = 4KB = 1 BRAM
  DICT_SIZE=4096 comparisons per byte
Dense memory encode[SIZE][256]
  12b node id (1.5B)
  Need 1.5*4096*256= 384*4KB = 384 BRAMs
  1 comparison and lookup per byte
  (maybe should be SIZE+256)

## Slide 55: 4K Chunk LZW Search
 | BRAMs | Operations/byte
Brute Search | 1 | 4K
Tree with Dense RAM | 384 | 1
36Kb BRAMs on ZU3EG = 216

## Slide 56: Complexity
Reminder from Day 15
  Optimized implementations tend to be more complex
  Large problems may force more complexity
    (e.g. Large window, deal with limited BRAMs on chip)
  Seeing examples of that today…

## Slide 57: Associative Memories
Part 3

## Slide 58: Associative Memory
Maps from a key to a value
Key not necessarily dense
  Contrast simple RAM
  Cannot afford 2256 word memory
Day 16 Review

## Slide 59: Associative Memories
Use for deduplication
Also may use in LZW to reduce BRAMs
  Just saw
    Problem: Simple 2D tree table requires too many BRAMs
    Opportunity: Tree table sparse

## Slide 60: Custom Hardware Associative Memory

## Slide 61: Memory Block Review
Match on address
Select wordline for a row
Reads out a word
Address dense and hardwired
One row for each 2Abits values
width
depth

## Slide 62: Address Blocks
Each address match is AND
width
depth
/A2&/A1&/A0
/A2&/A1&A0

## Slide 63: Address Blocks

## Slide 64: Memory Block Associative
Want address as key
Word is value
Key sparse
Rows<2keybits
Entries<2keybits
Key programmable
width
depth

## Slide 65: Programmable Key
Make row select programmable

## Slide 66: Contrast Assoc. and Dense Memory

## Slide 67: Associative Memory Bank

## Slide 68: Programmable Key
Assoc: 5b key, 8 entries, 8b value
How many memory bits?
Direct: 8 entries, 8b value
How many memory bits?

## Slide 69: Associative Memory Bank
Memory cells = entries*(keybits+valuebits)

## Slide 70: Associative Memory Bank
Will need to be able to write into key
  Another “fixed” decoder to generate key-word line for programming

## Slide 71: Associate Memory Cost
More expensive than equal capacity SRAM memory bank
  Memory cells in decoder
  Need to support write into key

## Slide 72: Associate Memory Cost
Physical associative memory for 4KB LZW Chunk tree encode
  4K entries
  12b (pos) output
  12b (pos)+8b (char)=20b key
Memory cells assoc.?
Compare direct 4Kx12 memory (cells)?
  How much larger is assoc. for same capacity?
Compare 4096*256 with 12b result for dense LZW case (cells)?
  How much larger to solve same problem

## Slide 73: Associative Memories FPGA
Part 4
(probably for Day 18)
Skip wrapup

## Slide 74: FPGA
Has BRAMs – normal memories, not associative
36Kb BRAM
  512x72
Can be 9b key  72b value assoc.
  Just using the memory sparsely
Or interpret as programmable decoder with 72 match lines

## Slide 75: Assoc. Mem from BRAM
For wider match
Cover 9b of key with each BRAM
Use 72 output bits to indicate if one of 72 entries match
AND together corresponding entries
Get 72 match bits
Re-encode match bits to lookup value

## Slide 76: BRAM Associative Memory
Previous slide expands match width
How would we expand capacity?
  Hint: how get a wider word (144b word)?

## Slide 77: BRAM Associative Memory

## Slide 78: Associative Memory Cost
Match unit
  Requires 1 BRAM per 9b of key per 72 entries
  ✖️
  Asymptotically optimal (keylen*entries)
    But large constants
  LZW
    4K entries
    20b key
    How many BRAMs for match?

## Slide 79: 4K LZW Chunk Search: Fully associative
Match BRAMs:
  Match key: 20b
  Entries: 4096
Value BRAMS:
  12b (state [position])
  12b x 4096 entries
  Takes 2 BRAMs

## Slide 80: Example Stored Values
Key[17:9] | Key[8:0] | Value
0x001 | 0x014 | 0x01
0x001 | 0x01 | 0x34
0x0F0 | 0x014 | 0xE3
0x0C8 | 0x113 | 0xCC

## Slide 81: Memory Contents
Addr | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
0x001 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1
0x014 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0x0C8 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0
0x0F0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0
0x113 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Addr | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
0x001 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0
0x014 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 1
0x0C8 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0x0F0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0x113 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0
Addr | Value
0x00 | 0x01
0x01 | 0x34
0x02 | 0xE3
0x03 | 0xCC
0x04 | 
0x05 | 
0x06 | 
(only show bottom 8 b; rest 0’s)
Value BRAM
Key[17:9] Match BRAM
Key[8:0] Match BRAM

## Slide 82: Code Snippet
ap_uint<72> key_low[512];
ap_uint<72> key_high[512];
int value[72];
match_low=key_low[key%512];
match_high=key_high[(key>>9)%512];
match=match_low & match_high;
addr=binary_encode(match);
res=value[addr];

## Slide 83: How Lookup Work?
Key[17:9] | Key[8:0] | Value
0x001 | 0x014 | 0x01
0x001 | 0x01 | 0x34
0x0F0 | 0x014 | 0xE3
0x0C8 | 0x113 | 0xCC
Lookup 0x214 = 0x001 0x014

## Slide 84: Code Snippet
ap_uint<72> key_low[512];
ap_uint<712> key_high[512];
int value[72];
match_low=key_low[key%512];
match_high=key_high[(key>>9)%512];
match=match_low & match_high;
addr=binary_encode(match);
res=value[addr];

## Slide 85: Memory Contents
Addr | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
0x001 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1
0x014 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0x0C8 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0
0x0F0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0
0x113 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Addr | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
0x001 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0
0x014 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 1
0x0C8 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0x0F0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0x113 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0
(only show bottom 8 b; rest 0’s)
Key[17:9] Match BRAM
Key[8:0] Match BRAM
match_low=key_low[key%512];
match_high=key_high[(key>>9)%512];
What match_low, match_high?

## Slide 86: Memory Contents
Addr | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
0x001 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1
0x014 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0x0C8 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0
0x0F0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0
0x113 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Addr | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
0x001 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0
0x014 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 1
0x0C8 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0x0F0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0x113 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0
(only show bottom 8 b; rest 0’s)
Key[17:9] Match BRAM
Key[8:0] Match BRAM
match_low=key_low[key%512];
match_high=key_high[(key>>9)%512];
match=match_low & match_high;
What match?

## Slide 87: What does binary_encode do?
binary_encode(0000000…010000)=0x40
10000…0  71
0000…01  0
0000…010  1
for (i=0<i<72;i++)
  If (bit[i]==1) return i
Return(MISS); // if not find (i.e., all 0’s)
Technicalities – maybe check only one 1

## Slide 88: Memory Contents
Addr | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
0x001 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1
0x014 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0x0C8 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0
0x0F0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0
0x113 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Addr | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
0x001 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0
0x014 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 1
0x0C8 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0x0F0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0x113 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0
(only show bottom 8 b; rest 0’s)
Key[17:9] Match BRAM
Key[8:0] Match BRAM
match_low=key_low[key%512];
match_high=key_high[(key>>9)%512];
match=match_low & match_high;
addr=binary_encode(match);
What addr?

## Slide 89: Memory Contents
Addr | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
0x001 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1
0x014 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0x0C8 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0
0x0F0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0
0x113 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Addr | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
0x001 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0
0x014 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 1
0x0C8 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0x0F0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0x113 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0
Addr | Value
0x00 | 0x01
0x01 | 0x34
0x02 | 0xE3
0x03 | 0xCC
0x04 | 
0x05 | 
0x06 | 
(only show bottom 8 b; rest 0’s)
Value BRAM
Key[17:9] Match BRAM
Key[8:0] Match BRAM
res=value[addr];
What res?

## Slide 90: How Lookup Work?
Key[17:9] | Key[8:0] | Value
0x001 | 0x014 | 0x01
0x001 | 0x01 | 0x34
0x0F0 | 0x014 | 0xE3
0x0C8 | 0x113 | 0xCC
Lookup 0x214 = 0x001 0x014

## Slide 91: Memory Contents
Addr | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
0x001 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1
0x014 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0x0C8 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0
0x0F0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0
0x113 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Addr | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
0x001 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0
0x014 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 1
0x0C8 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0x0F0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0x113 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0
Addr | Value
0x00 | 0x01
0x01 | 0x34
0x02 | 0xE3
0x03 | 0xCC
0x04 | 
0x05 | 
0x06 | 
(only show bottom 8 b; rest 0’s)
Value BRAM
Key[17:9] Match BRAM
Key[8:0] Match BRAM

## Slide 92: Add another entry
How BRAM contents change to add this entry
for 0x19001
match | Key[17:9] | Key[8:0] | Value
0 | 0x001 | 0x014 | 0x01
1 | 0x001 | 0x01 | 0x34
2 | 0x0F0 | 0x014 | 0xE3
3 | 0x0C8 | 0x113 | 0xCC
4 | 0x0C8 | 0x01 | 0x2B

## Slide 93: Memory Contents
Addr | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
0x001 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1
0x014 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0x0C8 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0
0x0F0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0
0x113 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Addr | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
0x001 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0
0x014 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 1
0x0C8 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0x0F0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0x113 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0
Addr | Value
0x00 | 0x01
0x01 | 0x34
0x02 | 0xE3
0x03 | 0xCC
0x04 | 
0x05 | 
0x06 | 
(only show bottom 8 b; rest 0’s)
Value BRAM
Key[17:9] Match BRAM
Key[8:0] Match BRAM

## Slide 94: Memory Contents
Addr | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
0x001 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1
0x014 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0x0C8 | 0 | 0 | 0 | 1 | 1 | 0 | 0 | 0
0x0F0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0
0x113 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Addr | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
0x001 | 0 | 0 | 0 | 1 | 0 | 0 | 1 | 0
0x014 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 1
0x0C8 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0x0F0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0x113 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0
Addr | Value
0x00 | 0x01
0x01 | 0x34
0x02 | 0xE3
0x03 | 0xCC
0x04 | 0x2B
0x05 | 
0x06 | 
(only show bottom 8 b; rest 0’s)
Value BRAM
Key[17:9] Match BRAM
Key[8:0] Match BRAM

## Slide 95: 4K Chunk LZW Search
 | BRAMs | Operations/byte
Brute Search | 1 | 4K
Tree with Dense RAM | 384 | 1
Tree with Full Assoc | 173 | 1
36Kb BRAMs on ZU3EG = 216

## Slide 96: Checkpoint
Notice levels of mapping:
  Prefix Tree algorithm
  Formulated on a 2D memory
  Then implemented in assoc. memory
    (later with Tree … hash table)

## Slide 97: Big Ideas
Can adaptively compress data using recurring substrings
  With constant work for symbol
Rich design space for engineering associative map solutions

## Slide 98: Admin
Feedback (including HW7)
Reading for Wednesday on Web
First project milestone due Friday
  Including teaming