## Slide 1: ESE5320: System-on-a-Chip Architecture
Day 18: Oct 30, 2024
Maps, Associative Memories, Hash Tables

## Slide 2: Today
Associative Memories on FPGAs (Part 1)
Software Map Trees (Part 2)
Hash Tables (Part 3)
  Software
  Hardware (FPGA) Hash Maps

## Slide 3: Message
Many options for Maps
Hash tables are useful tools

## Slide 4: Associative Memory
Maps from a key to a value
  associates a value with a key
Key not necessarily dense
  Contrast simple RAM
  Cannot afford 2256 word memory
Day 16 Review

## Slide 5: Associative Memories
Use for deduplication
Also may use in LZW to reduce BRAMs
  Just saw
    Problem: Simple 2D tree table requires too many BRAMs
    Opportunity: Tree table sparse

## Slide 6: Associative Memories FPGA
Part 1

## Slide 7: FPGA
Has BRAMs – normal memories, not associative
36Kb BRAM
  512x72
Can be 9b key  72b value assoc.
  Just using the memory sparsely
Or interpret as programmable decoder with 72 match lines

## Slide 8: Assoc. Mem from BRAM
For wider match
Cover 9b of key with each BRAM
Use 72 output bits to indicate if one of 72 entries match
AND together corresponding entries
Get 72 match bits
Re-encode match bits to lookup value

## Slide 9: What does binary_encode do?
binary_encode(0000000…010000)=0x40
10000…0  71
0000…01  0
0000…010  1
for (i=0<i<72;i++)
  If (bit[i]==1) return i
Return(MISS); // if not find (i.e., all 0’s)
Technicalities – maybe check only one 1

## Slide 10: BRAM Associative Memory
Previous slide expands match width
How would we expand capacity?
  Hint: how get a wider word (144b word)?

## Slide 11: BRAM Associative Memory

## Slide 12: Associative Memory Cost
Match unit
  Requires 1 BRAM per 9b of key per 72 entries
  ✖️
  Asymptotically optimal (keylen*entries)
    But large constants
  LZW
    4K entries
    20b key
    How many BRAMs for match?

## Slide 13: 4K LZW Chunk Search: Fully associative
Match BRAMs:
  Match key: 20b
  Entries: 4096
Value BRAMS:
  12b (state [position])
  12b x 4096 entries
  Takes 2 BRAMs

## Slide 14: 4K Chunk LZW Search
 | BRAMs | Operations/byte
Brute Search | 1 | 4K
Tree with Dense RAM | 384 | 1
Tree with Full Assoc | 173 | 1
36Kb BRAMs on ZU3EG = 216

## Slide 15: Example Stored Values
Key[17:9] | Key[8:0] | Value
0x001 | 0x014 | 0x01
0x001 | 0x01 | 0x34
0x0F0 | 0x014 | 0xE3
0x0C8 | 0x113 | 0xCC

## Slide 16: Memory Contents
Addr | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
0x001 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1
0x014 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0x0C8 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0
0x0F0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0
0x113 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Addr | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
0x001 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0
0x014 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 1
0x0C8 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0x0F0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0x113 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0
Addr | Value
0x00 | 0x01
0x01 | 0x34
0x02 | 0xE3
0x03 | 0xCC
0x04 | 
0x05 | 
0x06 | 
(only show bottom 8 b; rest 0’s)
Value BRAM
Key[17:9] Match BRAM
Key[8:0] Match BRAM

## Slide 17: Code Snippet
ap_uint<72> key_low[512];
ap_uint<72> key_high[512];
int value[72];
match_low=key_low[key%512];
match_high=key_high[(key>>9)%512];
match=match_low & match_high;
addr=binary_encode(match);
res=value[addr];

## Slide 18: How Lookup Work?
Key[17:9] | Key[8:0] | Value
0x001 | 0x014 | 0x01
0x001 | 0x01 | 0x34
0x0F0 | 0x014 | 0xE3
0x0C8 | 0x113 | 0xCC
Lookup 0x214 = 0x001 0x014

## Slide 19: Code Snippet
ap_uint<72> key_low[512];
ap_uint<712> key_high[512];
int value[72];
match_low=key_low[key%512];
match_high=key_high[(key>>9)%512];
match=match_low & match_high;
addr=binary_encode(match);
res=value[addr];

## Slide 20: Memory Contents
Addr | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
0x001 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1
0x014 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0x0C8 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0
0x0F0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0
0x113 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Addr | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
0x001 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0
0x014 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 1
0x0C8 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0x0F0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0x113 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0
(only show bottom 8 b; rest 0’s)
Key[17:9] Match BRAM
Key[8:0] Match BRAM
match_low=key_low[key%512];
match_high=key_high[(key>>9)%512];
What match_low, match_high?

## Slide 21: Memory Contents
Addr | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
0x001 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1
0x014 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0x0C8 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0
0x0F0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0
0x113 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Addr | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
0x001 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0
0x014 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 1
0x0C8 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0x0F0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0x113 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0
(only show bottom 8 b; rest 0’s)
Key[17:9] Match BRAM
Key[8:0] Match BRAM
match_low=key_low[key%512];
match_high=key_high[(key>>9)%512];
match=match_low & match_high;
What match?

## Slide 22: Memory Contents
Addr | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
0x001 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1
0x014 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0x0C8 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0
0x0F0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0
0x113 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Addr | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
0x001 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0
0x014 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 1
0x0C8 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0x0F0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0x113 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0
(only show bottom 8 b; rest 0’s)
Key[17:9] Match BRAM
Key[8:0] Match BRAM
match_low=key_low[key%512];
match_high=key_high[(key>>9)%512];
match=match_low & match_high;
addr=binary_encode(match);
What addr?

## Slide 23: Memory Contents
Addr | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
0x001 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1
0x014 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0x0C8 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0
0x0F0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0
0x113 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Addr | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
0x001 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0
0x014 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 1
0x0C8 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0x0F0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0x113 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0
Addr | Value
0x00 | 0x01
0x01 | 0x34
0x02 | 0xE3
0x03 | 0xCC
0x04 | 
0x05 | 
0x06 | 
(only show bottom 8 b; rest 0’s)
Value BRAM
Key[17:9] Match BRAM
Key[8:0] Match BRAM
res=value[addr];
What res?

## Slide 24: How Lookup Work?
Key[17:9] | Key[8:0] | Value
0x001 | 0x014 | 0x01
0x001 | 0x01 | 0x34
0x0F0 | 0x014 | 0xE3
0x0C8 | 0x113 | 0xCC
Lookup 0x1E14 = 0x0F0 0x014

## Slide 25: Memory Contents
Addr | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
0x001 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1
0x014 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0x0C8 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0
0x0F0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0
0x113 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Addr | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
0x001 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0
0x014 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 1
0x0C8 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0x0F0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0x113 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0
Addr | Value
0x00 | 0x01
0x01 | 0x34
0x02 | 0xE3
0x03 | 0xCC
0x04 | 
0x05 | 
0x06 | 
(only show bottom 8 b; rest 0’s)
Value BRAM
Key[17:9] Match BRAM
Key[8:0] Match BRAM

## Slide 26: Add another entry
How BRAM contents change to add this entry
for 0x19001
match | Key[17:9] | Key[8:0] | Value
0 | 0x001 | 0x014 | 0x01
1 | 0x001 | 0x01 | 0x34
2 | 0x0F0 | 0x014 | 0xE3
3 | 0x0C8 | 0x113 | 0xCC
4 | 0x0C8 | 0x01 | 0x2B

## Slide 27: Memory Contents
Addr | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
0x001 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1
0x014 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0x0C8 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0
0x0F0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0
0x113 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Addr | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
0x001 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0
0x014 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 1
0x0C8 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0x0F0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0x113 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0
Addr | Value
0x00 | 0x01
0x01 | 0x34
0x02 | 0xE3
0x03 | 0xCC
0x04 | 
0x05 | 
0x06 | 
(only show bottom 8 b; rest 0’s)
Value BRAM
Key[17:9] Match BRAM
Key[8:0] Match BRAM

## Slide 28: Memory Contents
Addr | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
0x001 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1
0x014 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0x0C8 | 0 | 0 | 0 | 1 | 1 | 0 | 0 | 0
0x0F0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0
0x113 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Addr | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
0x001 | 0 | 0 | 0 | 1 | 0 | 0 | 1 | 0
0x014 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 1
0x0C8 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0x0F0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0x113 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0
Addr | Value
0x00 | 0x01
0x01 | 0x34
0x02 | 0xE3
0x03 | 0xCC
0x04 | 0x2B
0x05 | 
0x06 | 
(only show bottom 8 b; rest 0’s)
Value BRAM
Key[17:9] Match BRAM
Key[8:0] Match BRAM

## Slide 29: Checkpoint
Notice levels of mapping:
  Prefix Tree algorithm
  Formulated on a 2D memory
  Then implemented in assoc. memory
    (later with Tree … hash table)

## Slide 30: 4K Chunk LZW Search Story so far….
 | BRAMs | Operations/byte
Brute Search | 1 | 4K
Tree with Dense RAM | 384 | 1
Tree with Full Assoc | 173 | 1
36Kb BRAMs on ZU3EG = 216

## Slide 31: Software Map
Part 2

## Slide 32: Software Map
Map abstraction
  void insert(key,value);
  value lookup(key);
Will typically have many different implementations

## Slide 33: Preclass 3
For a capacity of 4096
How many memory accesses needed
  When lookup fail?
  When lookup succeed (on average)?

## Slide 34: Tree Map (Preclass 5)
Build search tree
Walk down tree
For a capacity of 4096, assume balanced…
How many tree nodes visited
  When lookup fail?
  When lookup succeed (on average)?

## Slide 35: Tree Map LZW
Each character requires log2(dict) lookups
  12 for 4096
Each internal tree node hold
  Key (20b for LZW), value (12b), and 2 pointers (12b)
  7B
Total nodes 4K*2
Need 14 BRAMs for 4K chunk

## Slide 36: Tree Insert
Need to maintain balance
Doable with O(log(N)) insert
  Tricky
  See Red-Black Tree
    https://en.wikipedia.org/wiki/Red–black_tree
    https://www.geeksforgeeks.org/red-black-tree-set-1-introduction-2/

## Slide 37: 4K Chunk LZW Search Story so far….
 | BRAMs | Operations/byte
Brute Search | 1 | 4K
Tree with Dense RAM | 384 | 1
Tree with Full Assoc | 173 | 1
Tree with Tree | 14 | 12
36Kb BRAMs on ZU3EG = 216

## Slide 38: Hash Tables
Part 3

## Slide 39: High Performance Map
Would prefer not to search
Want to do better than log2(N) time
  log2(N) achieved with tree
Direct lookup in arrays (memory) is good…

## Slide 40: Hash Table
Attempt to turn into direct lookup
Compute some function of key
  A hash
Perform lookup at that point
If hash maps a single entry (or no entry)
  Great, got direct lookup
    Like sparse table case
hash
Mem
lookup_key
match_key, value
Miss =
(match_key!=lookup_key)

## Slide 41: Hash Entries
Average number of entries per hash when N > HASH_CAPACITY?
  Concrete example
    N= 4096
    HASH_CAPACITY=256

## Slide 42: Preclass 1
Collect distribution for student name hashes

## Slide 43: Hash Table
Attempt to turn into direct lookup
Compute some function of key
  A hash
Perform lookup at that point
Typically, prepared for several keys to map to same hash  call it a bucket
  Keep list or tree of things in each bucket
hash
Mem
lookup_key
Bucket =
<k1,v1>,
<k2,v2>,
<k3,v3>

## Slide 44: Hash Table
Compute some function of key
  A hash
Perform lookup at that point
Find bucket with small number of entries
  Searching that bucket easier
  …but no absolute guarantee on maximum bucket size
hash
Mem
Bucket =
<k1,v1>,
<k2,v2>,
<k3,v3>
lookup_key

## Slide 45: Hardware Hash Tables

## Slide 46: Hardware Hash
Want to avoid variable size buckets
  So can read in one lookup
    Can make wider for some fixed number of slots
  So can resolve in one cycle
hash
Mem
Bucket =
<k1,v1>,
<k2,v2>,
<k3,v3>
lookup_key

## Slide 47: Hash Size Distribution
Look at what the distribution looks like for number of entries
N – number of entries
C – HASH_CAPACITY (N<C) [buckets]
m – number of items mapped to a bucket
Compute distribution for each bucket size (m)

## Slide 48: Preclass 4
m | 0 | 1 | 2 | 3 | 4+
C=1024 |  |  |  |  | 
C=2048 |  | 0.30 |  |  | 
C=4096 |  |  |  |  | 
N=1024

## Slide 49: Preclass 4
m | 0 | 1 | 2 | 3 | 4+
C=1024 | 0.37 | 0.37 | 0.18 | 0.061 | 0.019
C=2048 | 0.60 | 0.30 | 0.076 | 0.013 | 0.0017
C=4096 | 0.78 | 0.19 | 0.024 | 0.0020 | 0.00013
N=1024
Note: 2 design axes here

## Slide 50: Hash
Can tune hash parameters to control distribution
Spend more memory  smaller buckets  less work finding things in buckets
  Memory-Time tradeoff
Still have possibility of large buckets
  …but probability is low

## Slide 51: Idea
Hash mostly works
Engineer hash to hold most cases
  Combination of
    sparcity (entries>N)
    Hold multiple entries per hash value
Few cases that overflow
  Store in small fully associative memory

## Slide 52: Hybrid Hash+Assoc.

## Slide 53: LZW 4K Chunk Hybrid
72 entry assoc. match
  needs 3 match BRAMs + 1 value BRAM
  Associative match 20b key
  72 entries (72/4096=1.7% for 4096)
So, can hold ~1% conflicts in 4K hash
Hash N=4096, C=16384, m=2, store 2
  Prob 3+: <1% (see table 1024, 4096)
    )0.002+0.000013)*4096 < 9 entries overlfow
  20b key+12b value=4B per entry
  16384*2*4B=4*2*4 BRAMs
32+4=36 BRAMs

## Slide 54: Further Optimization
Previous example illustrative
  Not necessarily optimal (explore parameters)
    Expect not optimal
May be able to do better with multiple hashes
  See Dhawan reading paper
  May need to use that design in hybrid configuration with assoc. memory like previous example

## Slide 55: Allow Imperfect?
Question: impact on compression if cannot store a few tree entries?
Some encodings will find shorter matches than optimal
Q: Impact on compression rate as a function of conflict rate?
How compare to compression rate impact of chunk size?
  Larger chunk with conflict rate vs. smaller chunk with smaller (or no) conflict rate
 another tradeoff to explore

## Slide 56: Hash Complexity
Want to compute these lookup hashes for hardware fast
  In a single cycle to keep II down for LZW
  Can xor-together a set of bits quickly in hardware
    Any 6-bits for one output bit in a single 6-LUT
    Means capacity must be power-of-2

## Slide 57: 4K Chunk LZW Search
 | BRAMs | Operations/byte
Brute Search | 1 | 4K
Tree with Dense RAM | 384 | 1
Tree with Full Assoc | 173 | 1
Tree with Tree | 14 | 12
Tree with Hybrid Hash | 36 | 1
36Kb BRAMs on ZU3EG = 216

## Slide 58: Big Ideas
Many ways to implement maps
Near O(1) Map access  Hash Table

## Slide 59: Admin
Feedback
Reading for Monday on web
First project milestone due Friday
  Including teaming
  Need teaming sort out board shuffle
P2 out