## Slide 1: ECE 252 / CPS 220 Advanced Computer Architecture I Lecture 14 Virtual Memory
Benjamin Lee
Electrical and Computer Engineering
Duke University
www.duke.edu/~bcl15
www.duke.edu/~bcl15/class/class_ece252fall11.html

## Slide 2
ECE252 Administrivia
20 October – Project Proposals Due
  One page proposal
  What question are you asking?
  How are you going to answer that question?
  Talk to me if you are looking for project ideas.
25 October – Homework #3 Due
25 October – Class Discussion
Roughly one reading per class. Do not wait until the day before!
  Jouppi. “Improving direct-mapped cache performance by the addition of a small fully-associative cache and prefetch buffers.”
  Kim et al. “An adaptive, non-uniform cache structure for wire-delay dominated on-chip caches.”
  Fromm et al. “The energy efficiency of IRAM architectures”
  Lee et al. “Phase change memory architecture and the quest for scalability”

## Slide 3
Last Time
Caches
  Quantify cache/memory hierarchy with AMAT
  Three types of cache misses: (1) compulsory, (2) capacity, (3) conflict
  Cache structure and data placement policies determine miss rates
  Write buffers improve performance
Prefetching
  Identify and exploit spatial locality
  Prefetchers can be implemented in hardware, software, both
Caches and Code
  Restructuring SW code can improve HW cache performance
  Data re-use can improve with code structure (e.g., matrix multiply)

## Slide 4
Physical Addresses
One program runs at a time. Program has unrestricted access to machine (RAM, I/O)
Program addresses depend on where program is loaded into memory
But programmers do not think about memory addresses when writing sub-routines…
  How is location independence achieved? Loader/Linker
  (1) loads sub-routines into memory, determines physical addresses,
  (2) links multiple sub-routines,
  (3) resolves physical addresses so jumps to sub-routines go to correct memory locations

## Slide 5
Machine with Physical Addresses
With unrestricted access to a machine, program uses physical addresses.
PC
Inst. Cache
D
Decode
E
M
Data Cache
W
+
Main Memory (DRAM)
Memory Controller
Physical Address
Physical Address
Physical Address
Physical Address
Physical Address

## Slide 6
Address Translation
Motivation
In early machines, I/O is slow and requires processor support
Increase throughput by over-lapping I/O for multiple programs
Eliminate processor support with direct memory access (DMA)
DMA: (1) Processor initiates I/O, (2) Processor does other operations during transfer, (3) Processor receives interrupt from DMA controller when transfer is complete
Location-Independent Programs
  Simplify program and storage management
Protection
Independent programs should not affect others (isolated memory spaces)
Multi-programming requires “supervisor” to schedule programs, manage context switches between programs
prog1
prog2
Physical Memory
OS

## Slide 7
Virtual and Physical Memory
Programs receive allocations of physical memory at specific physical addresses.
Program operates in virtual memory with virtual addresses.
Memory Management Unit (MMU) – performs address translation to map virtual addresses to physical addresses.
Virtual Memory
Physical Memory

## Slide 8
1 - Base & Bound
Base register – Identifies a program’s allocation in physical memory.
Bound register – Provides protection and isolation between programs
Base, Bound registers visible only when processor is running in “supervisor” mode
Virtual Memory
Program Address Space
Bound Register

Bounds
Violation?
Physical Memory
current
segment
Base Register
+
Physical
Address
Virtual Address
Base Physical Address
Segment Length

## Slide 9
Machine with Virtual Addresses
Every access to memory requires translating virtual addresses to physical addresses. Efficient adder implementations are possible for (base+offset).
PC
Inst. Cache
D
Decode
E
M
Data Cache
W
+
Main Memory (DRAM)
Memory Controller
Physical Address
Physical Address
Physical Address
Physical Address
Data Bound Register
Data Base Register

+
Logical Address
Bounds Violation?
Physical Address
Prog. Bound Register
Program Base Register

+
Logical Address
Bounds Violation?

## Slide 10
Base & Bounds Implementation
Hardware Cost
Two registers, adder, comparator
Fast logic
Context Switch
Save/restore base, bound registers

## Slide 11
2 - Segmentation
Motivation
  Separate virtual address space into several segments.
  Each segment is contiguous but segments may be fragmented.
  Segmentation does not require fully contiguous address space (i.e., allow holes in address space)
Idea
  Generalize Base & Bounds
  Implement a table of base-bound pairs
  Virtual Segment # Physical Segment Base Segment Size
  Code (00) 0x4000 0x700
  Data (01) 0x0000 0x500
  - (10) 0 0
  Stack (11) 0x2000 0x1000

## Slide 12
Data & Program Segments
What is the advantage of this separation?
Physical Address
Physical Address
Virtual Memory
Program Address
Space
Main Memory
data
segment
Data Bound Register
Mem. Address Register
Data Base Register

+
Bounds
Violation?
Program Bound Register
Program Counter
Program Base Register

+
Bounds
Violation?
program
segment
Logical Address
Logical Address

## Slide 13
Segmentation Implementation
Virtual Address
  Partition into segment and offset
  Segment – Specifies segment number, which indexes table
  Offset – Specifies offset within a segment
Segment Table
  Segment – Provides segment base
  Size – Provides segment bound
Translation
  Compute physical address from segment base, offset, and bound

## Slide 14
Fragmentation
As programs enter and leave the system, physical memory is fragmented.
Fragmentation occurs because segments are variable size
OS
Space
16K
32K
user 1
user 2
user 3
OS
Space
16K
16K
24K
user 1
user 2
user 3
user 5
user 4
8K
Users 4 & 5
arrive
Users 2 & 5
leave
OS
Space
16K
24K
16K
24K
user 1
user 4
8K
user 3
free
24K
24K
24K
24K
32K
32K

## Slide 15
3 - Paging
Motivation
  Branch&Bounds, Segmentation require fancy memory management
  Example: What mechanism coalesces free fragments?
Idea
  Constrain segmentation with fixed-size segments (e.g., pages)
  Paging simplifies memory management
  Example: free page management is a simple bitmap
  00111111100000011100
  Each bit represents on page of physical memory
  1 means allocated, 0 means free

## Slide 16
Paging Implementation
Virtual Address
  Partition into page and offset
  Page – Specifies virtual page number, which indexes table
  Offset – Specifies offset within a page
Page Table
  Page – Provides a physical page number
  Size – No longer required, all pages equal size (e.g., 4KB)
Translation
  Compute physical address from physical page number, offset

## Slide 17
4 – Segmentation & Paging
Motivation
  Assume 32-bit virtual addresses, 4KB page size
  4KB = 4096 bytes = 212 bytes per page
  212 bytes per page requires a 12-bit offset
  Remaining address bits used for page number, 20-bit page number
  Page tables can be very large.
  With 20-bit page number, 220 pages
  Each program in multi-programmed machine requires its own page table
  Total size of page tables = [# of programs] x 220
Idea
  Combine segmentation with paging
  Adds indirection to reduce size of page table

## Slide 18
Segmented Page Tables
Virtual Address
  Partition into segment, page, offset
  Segment –Specifies segment#, which indexes Table 1
  Page – Specifies virtual page # number, which indexes Table 2
  Offset – Specifies offset in page
Table 1
  Segment – Points to a page table
  Size – Specifies number of pages in segment
Table 2
  Page – Provides a physical page#
Translation
  Compute physical address from physical page number, offset
What about paged page tables?

## Slide 19
Address Translation & Protection
  Every access to instruction/data memory requires (1) address translation and (2) protection checks
  A good virtual memory system must be fast (completing in approximately 1 cycle) and space efficient
Physical Address
Virtual Address
Address
Translation
Virtual Page No. (VPN)
offset
Physical Page No. (PPN)
offset
Protection
Check
Exception?
Kernel/User Mode
Read/Write

## Slide 20
Translation Lookaside Buffer (TLB)
Address Translation is Expensive
  In a two-level page table, each reference requires several memory accesses.
Solution
    Cache translations. We use a data structure called a TLB.
    TLB Hit – single cycle translation
    TLB Miss – walk page table to translate, update TLB
VPN offset
tag PPN
physical address
PPN offset
virtual address
hit?
(VPN = virtual page number)
(PPN = physical page number)

## Slide 21
TLB Design
32-128 entries, fully associative
  Each entry maps a large page. Little spatial locality across 4KB pages. Conflicts are more likely.
  Larger TLBs (e.g., 256-512 entries) may be 4-8 way set-associative
  Even larger systems may have multi-level TLBs
Random or FIFO replacement policies
Definition – TLB Reach
    Size of largest virtual address space that can be simultaneously mapped
    64 entries, 4KB pages, 1 page per entry
    TLB Reach = [64 entries] x [4KB] = 256KB (if pages contiguous in memory)

## Slide 22
TLB Misses
Software (MIPS, Alpha)
  TLB miss causes an exception
  Operating system walks page table and reloads TLB
  Requires privileged processor mode. Why?
Hardware (SPARC v8, x86, PowerPC)
    Memory management unit (MMU) walks page table and reloads TLB
    If MMU encounters missing page, MMU causes an exception
    Operating system handles page fault, which requires transferring page from disk to memory.

## Slide 23
Machine with Virtual Memory
PC
Inst. TLB
Inst. Cache
D
Decode
E
M
Data Cache
W
+
Page Fault?
Protection violation?
Page Fault?
Protection violation?
Data TLB
Main Memory (DRAM)
Memory Controller
Physical Address
Physical Address
Physical Address
Physical Address
Page-Table Base Register
Virtual Address
Physical Address
Virtual Address
Hardware Page Table Walker
Miss?
Miss?

## Slide 24
Address Translation Summary
virtual address
TLB
Lookup
Page Table
Walk
update TLB
page fault
(OS loads page)
Protection
Check
physical address
(use to access L1 cache)
miss
hit
denied
permitted
protection
fault
hardware
hardware or software
software
exception
handler
page
in mem
page not
in mem
seg fault

## Slide 25
Summary
Virtual Memory
  Enables multi-programming
  Programs operate in virtual memory space
  Programs are protected from each other
Virtual to Physical Address Translation
  Base&Bound
  Segmentation
  Paging
  Multi-level Translation (segmented paging, paged paging)
Translation Lookaside Buffer
  Accelerates virtual memory, address translation

## Slide 26
Acknowledgements
    These slides contain material developed and copyright by
    Arvind (MIT)
    Krste Asanovic (MIT/UCB)
    Joel Emer (Intel/MIT)
    James Hoe (CMU)
    Arvind Krishnamurthy (U. Washington)
    John Kubiatowicz (UCB)
    Alvin Lebeck (Duke)
    David Patterson (UCB)
    Daniel Sorin (Duke)