## Slide 1: ECE 252 / CPS 220 Advanced Computer Architecture I Lecture 14 Very Long Instruction Word Machines
Benjamin Lee
Electrical and Computer Engineering
Duke University
www.duke.edu/~bcl15
www.duke.edu/~bcl15/class/class_ece252fall11.html

## Slide 2
ECE252 Administrivia
15 November – Homework #4 Due
  Will be posted by end of week.
Project Proposals
  Should have received comments already.
ECE 299 – Energy-Efficient Computer Systems
  www.duke.edu/~bcl15/class/class_ece299fall10.html
  Technology, architectures, systems, applications
  Seminar for Spring 2012.
  Class is paper reading, discussion, research project
  In Fall 2010, students read >35 research papers.
  In Fall 2012, read research papers.
  In Fall 2012, also considering textbook “The Datacenter as a Computer: An Introduction to the Design of Warehouse-scale Machines.”

## Slide 3
Last Time
Virtual Memory
  Enables multi-programming
  Programs operate in virtual memory space
  Programs are protected from each other
Virtual to Physical Address Translation
  Base&Bound
  Segmentation
  Paging
  Multi-level Translation (segmented paging, paged paging)
Translation Lookaside Buffer
  Accelerates virtual memory, address translation

## Slide 4
OoO Superscalar Complexity
Out-of-order Superscalar
  Objective: Increase instruction-level parallelism.
  Cost: Hardware logic/mechanisms to track dependencies and dynamically schedule independent instructions.
Hardware Complexity
  Instructions can issue, complete out-of-order.
  Instructions must commit in-order
  Implement Tomasulo’s algorithm with a variety of structures
  Example: Reservation stations, reorder buffer, physical register file
Very Long Instruction Word (VLIW)
  Objective: Increase instruction-level parallelism.
  Cost: Software compilers/mechanisms to track dependencies and statically schedule independent instructions.

## Slide 5
Review of Fetch/Decode
Fetch
  Load instruction by accessing memory at program counter (PC)
  Update PC using sequential address (PC+4) or branch prediction (BTB)
Decode/Rename
  Take instruction from fetch buffer
  Allocate resources, which are necessary to execute instruction:
    (1) Destination physical register – if instruction writes a register, rename
    (2) Reorder buffer (ROB) entry – support in-order commit
    (3) Issue queue entry – hold instruction as it waits for execution
    (4) Memory buffer entry – resolve dependencies through memory (next slide)
  Stall if resources unavailable
  Rename source/destination registers
  Update reorder buffer, issue queue, memory buffer

## Slide 6
Review of Memory Buffer
Allocate memory buffer entry
Store Instructions
  Calculate store-address and place in buffer
  Take store-data and place in buffer
  Instruction commits in-order when store-address, store-data ready
Load Instructions
  Calculate load-address and place in buffer
  Instruction searches memory buffer for stores with matching address
  Forward load data from in-flight stores with matching address
  Stall load if buffer contains stores with un-resolved addresses

## Slide 7
Review of Issue/Execute
Issue
  Instruction commits from reorder buffer
  A commit wakes-up an instruction by marking its sources ready
  Select logic determines which ready instructions should execute
  Issue when by sending instructions to functional unit
Execute
  Read operands from physical register file and/or forwarding path
  Execute instruction in functional unit
  Write result to physical register file, store buffer
  Produce exception status
  Write to reorder buffer

## Slide 8
Review of Commit
Commit
  Instructions can complete and update reorder buffer out-of-order
  Instructions commit from reorder buffer in-order
Exceptions
  Check for exceptions
  If exception raised, flush pipeline
  Jump to exception handler
Release Resources
  Free physical register used by last writer to same architected register
  Free reorder buffer slot
  Free memory buffer slot

## Slide 9
Control Logic Scaling
Lifetime (L) – number of cycles an instruction spends in pipeline
Lifetime depends on pipeline latency, time spent in reorder buffer
Issue width (W) – maximum number of instructions issued per cycle
As W increases, issue logic must find more instructions to execute in parallel and keep pipeline busy.
More instructions must be fetched, decoded, and queued.
W x L instructions can impact any of the W issuing instructions (e.g. forwarding) and growth in hardware proportional to W x (W x L)
Lifetime L
Issue Group
Previously Issued Instructions
Issue Width W

## Slide 10
Control Logic (MIPS R10000)
Control Logic

## Slide 11
Sequential Instruction Sets
Check instruction dependencies
Superscalar processor
a = foo(b);
for (i=0, i<
Sequential source code
Superscalar compiler
Find independent operations
Schedule operations
Sequential machine code
Schedule execution

## Slide 12
Sequential Instruction Sets
Superscalar Compiler
  Takes sequential code (e.g., C, C++)
  Check instruction dependencies
  Schedule operations to preserve dependencies
  Produces sequential machine code (e.g., MIPS)
Superscalar Processor
  Takes sequential code (e.g., MIPS)
  Check instruction dependencies
  Schedule operations to preserve dependencies
Inefficiency of Superscalar Processors
  Performs dependency, scheduling dynamically in hardware
  Expensive logic rediscovers schedules that a compiler could have found

## Slide 13
VLIW – Very Long Instruction Word
Multiple operations packed into one instruction format
Instruction format is fixed, each slot supports particular instruction type
Constant operation latencies are specified (e.g., 1 cycle integer op)
Software schedules operations into instruction format, guaranteeing
  Parallelism within an instruction – no RAW checks between ops
  No data use before ready – no data interlocks/stalls
Two Integer Units,
Single Cycle Latency
Two Load/Store Units,
Three Cycle Latency
Two Floating-Point Units,
Four Cycle Latency
Int Op 2
Mem Op 1
Mem Op 2
FP Op 1
FP Op 2
Int Op 1

## Slide 14
VLIW Compiler Responsibilities
Schedule operations to maximize parallel execution
  Fill operation slots
Guarantee intra-instruction parallelism
  Ensure operations within same instruction are independent
Schedule to avoid data hazards
  Separate options with explicit NOPs

## Slide 15
Loop Execution
for (i=0; i<N; i++)
B[i] = A[i] + C;
Int1
Int 2
M1
M2
FP+
FPx
loop:
ld
add r1
fadd
sd
add r2
bne
loop: ld f1, 0(r1)
add r1, 8
fadd f2, f0, f1
sd f2, 0(r2)
add r2, 8
bne r1, r3, loop
Compile
Schedule
The latency of each instruction is fixed (e.g., 3 cycle ld, 4 cycle fadd)
Instr-1: Load A[i] and increment i (r1) in parallel
Instr-2: Wait for load
Instr-3: Wait for add. Store B[i], increment i (r2), branch in parallel
How many flops / cycle? 1 fadd / 8 cycles = 0.125

## Slide 16
Loop Unrolling
Unroll inner loop to perform k iterations of computation at once.
If N is not a multiple of unrolling factor k, insert clean-up code
Example: unroll inner loop to perform 4 iterations at once
for (i=0; i<N; i++)
B[i] = A[i] + C;
for (i=0; i<N; i+=4)
{
B[i] = A[i] + C;
B[i+1] = A[i+1] + C;
B[i+2] = A[i+2] + C;
B[i+3] = A[i+3] + C;
}

## Slide 17
Scheduling Unrolled Loops
loop: ld f1, 0(r1)
ld f2, 8(r1)
ld f3, 16(r1)
ld f4, 24(r1)
add r1, 32
fadd f5, f0, f1
fadd f6, f0, f2
fadd f7, f0, f3
fadd f8, f0, f4
sd f5, 0(r2)
sd f6, 8(r2)
sd f7, 16(r2)
sd f8, 24(r2)
add r2, 32
bne r1, r3, loop
schedule
Int1
Int 2
M1
M2
FP+
FPx
loop:
ld f1
ld f2
ld f3
ld f4
add r1
fadd f5
fadd f6
fadd f7
fadd f8
sd f5
sd f6
sd f7
sd f8
add r2
bne
Unroll loop to execute 4 iterations
Reduces number of empty operation slots
How many flops/cycle? 4 fadds / 11 cycles = 0.36

## Slide 18
Software Pipelining
Exploit independent loop iterations
  If loop iterations are independent, then get more parallelism by scheduling instructions from different iterations
  Example: Loop iterations are independent in the code sequence below.
  Construct the data-flow graph for one iteration
load A[i]
C
+
store B[i]
for (i=0; i<N; i++)
B[i] = A[i] + C;

## Slide 19
Software Pipelining (Illustrated)
Not pipelined
load A[0]
C
+
store B[0]
load A[1]
C
+
store B[1]
load A[2]
C
+
store B[2]
load A[3]
C
+
store B[3]
Fill
Steady State
Drain
Pipelined
Load A[0]
C
+
load A[1]
C
store B[0]
+
load A[2]
C
store B[1]
+
load A[3]
C
store B[2]
+
load A[4]
C
store B[3]
+
load A[5]
C
store B[4]
+
store B[5]

## Slide 20
Scheduling SW Pipelined Loops
Unroll the loop to perform 4 iterations at once. Then SW pipeline.
for (i=0; i<N; i++)
B[i] = A[i] + C;
loop: ld f1, 0(r1)
ld f2, 8(r1)
ld f3, 16(r1)
ld f4, 24(r1)
add r1, 32
fadd f5, f0, f1
fadd f6, f0, f2
fadd f7, f0, f3
fadd f8, f0, f4
sd f5, 0(r2)
sd f6, 8(r2)
sd f7, 16(r2)
add r2, 32
sd f8, -8(r2)
bne r1, r3, loop
Int1
Int 2
M1
M2
FP+
FPx
ld f1
ld f2
ld f3
ld f4
fadd f5
fadd f6
fadd f7
fadd f8
sd f5
sd f6
sd f7
sd f8
add r1
add r2
bne
ld f1
ld f2
ld f3
ld f4
fadd f5
fadd f6
fadd f7
fadd f8
sd f5
sd f6
sd f7
sd f8
add r1
add r2
bne
ld f1
ld f2
ld f3
ld f4
fadd f5
fadd f6
fadd f7
fadd f8
sd f5
add r1
loop:
steady
state
fill
drain

## Slide 21
Unrolling versus Pipelining
  Unrolled loops pay fill and drain costs once per loop iteration.
  SW pipelined loops pay (a.k.a. prologue) and drain (a.k.a. epilogue) costs only once per loop.
time
performance
time
performance
Loop Unrolled
Software Pipelined
Wind-down overhead
Loop Iteration
Loop Iteration

## Slide 22
What if there are no loops?
  Basic block defined by sequence of consecutive instructions. Every basic block ends with a branch.
  Instruction-level parallelism is hard to find in basic blocks
  Basic blocks illustrated by control flow graph
Basic block

## Slide 23
Trace Scheduling
  A trace is a sequence of basic blocks (a.k.a., long string of straight-line code)
  Trace Selection: Use profiling or compiler heuristics to find common sequences/paths
  Trace Compaction: Schedule whole trace into few VLIW instructions.
  Add fix-up code to cope with branches jumping out of trace. Undo instructions if control flower diverges from trace.

## Slide 24
Problems with “Classic” VLIW
Object Code Challenges
  Compatibility: Need to recompile code for every VLIW machine, even across generations.
  Compatibility: Code specific to operation slots in instruction format and latencies of operations
  Code Size: Instruction padding wastes instruction memory/cache with nops for unfilled slots.
  Code Size: Loop unrolling, software pipelining increases code footprint.
Scheduling Variable Latency Operations
  Effective schedules rely on known instruction latencies
  Caches, memories produce unpredictable variability

## Slide 25
Problems with “Classic” VLIW
Object Code Challenges
  Compatibility: Need to recompile code for every VLIW machine, even across generations.
  Compatibility: Code specific to operation slots in instruction format and latencies of operations
  Code Size: Instruction padding wastes instruction memory/cache with nops for unfilled slots.
  Code Size: Loop unrolling, software pipelining increases code footprint.
Scheduling Variable Latency Operations
  Effective schedules rely on known instruction latencies
  Caches, memories produce unpredictable variability

## Slide 26
Intel Itanium, EPIC IA-64
Explicitly Parallel Instruction Computing (EPIC)
  Computer architecture style (e.g., CISC, RISC, EPIC)
IA-64
  Instruction set architecture (e.g., x86, MIPS, IA-64)
  IA-64 – Intel Architecture 64-bit
Implementations
  Merced, first implementation, 2001
  McKinley, second implementation, 2002
  Poulson, recent implementation, 2011

## Slide 27
Intel Itanium, EPIC IA-64
Eight cores
1-cycle 16KB L1 I&D caches
9-cycle 512KB L2 I-cache
8-cycle 256KB L2 D-cache
32 MB shared L3 cache
544mm2 in 32nm CMOS
3 billion transistors
Cores are 2-way multithreaded
Each VLIW word is 128-bits, containing 3 instructions (op slots)
Fetch 2 words per cycle  6 instructions (op slots)
Retire 4 words per cycle  12 instructions (op slots)

## Slide 28
Intel Itanium, EPIC IA-64
Template bits describe grouping of these instructions with others in adjacent bundles
Each group contains instructions that can execute in parallel
Instruction 2
Instruction 1
Instruction 0
Template
128-bit instruction bundle
group i
group i+1
group i+2
group i-1
bundle j
bundle j+1
bundle j+2
bundle j-1

## Slide 29
VLIW and Control Flow Challenges
Challenge
  Mispredicted branches limit ILP
  Trace selection groups basic blocks into larger ones
  Trace compaction schedules instructions into a single VLIW
  Requires fix-up code for branches that exit trace
Solution – Predicated Execution
  Eliminate hard to predict branches with predicated execution
  IA-64 instructions can be executed conditionally under predicate
  Instruction becomes a NOP if predicate register is false

## Slide 30
VLIW and Control Flow Challenges
Inst 1
Inst 2
br a==b, b2
Inst 3
Inst 4
br b3
Inst 5
Inst 6
Inst 7
Inst 8
b0:
b1:
b2:
b3:
if
else
then
Four basic blocks
Inst 1
Inst 2
p1,p2 <- cmp(a==b)
(p1) Inst 3 || (p2) Inst 5
(p1) Inst 4 || (p2) Inst 6
Inst 7
Inst 8
Predication
One basic block
On average >50% branches removed. Mahlke et al. 1995.

## Slide 31
Limits of Static ILP
Software Instruction-level Parallelism (VLIW)
  Compiler complexity
  Code size explosion
  Unpredictable branches
  Variable memory latency and unpredictable cache behavior
Current Status
  Despite several attempts, VLIW has failed in general-purpose computing
  VLIW hardware complexity similar to in-order, superscalar hardware complexity. Limited advantage on large, complex applications
  Successful in embedded digital signal processing; friendly code

## Slide 32
Summary
Out-of-order Superscalar
  Hardware complexity increases super-linearly with issue-width.
Very Long Instruction Word (VLIW)
  Compiler explicitly schedules parallel instructions
  Unrolling and software pipelining loops
Predication
  Mitigates branches in VLIW machines
  Add predicates to operations.
  If predicate is false, instruction does not affect architected state
  Mahlke et al. “A comparison of full and partial predicated execution support for ILP processors” 1995.

## Slide 33
Acknowledgements
    These slides contain material developed and copyright by
    Arvind (MIT)
    Krste Asanovic (MIT/UCB)
    Joel Emer (Intel/MIT)
    James Hoe (CMU)
    Arvind Krishnamurthy (U. Washington)
    John Kubiatowicz (UCB)
    Alvin Lebeck (Duke)
    David Patterson (UCB)
    Daniel Sorin (Duke)