## Slide 1: ECE 552 / CPS 550 Advanced Computer Architecture I Lecture 10 Instruction-Level Parallelism – Part 3
Benjamin Lee
Electrical and Computer Engineering
Duke University
www.duke.edu/~bcl15
www.duke.edu/~bcl15/class/class_ece252fall12.html

## Slide 2
ECE552 Administrivia
27 September – Homework #2 Due
  Assignment on web page. Teams of 2-3.
  Submit soft copies to Sakai.
  Use Piazza for questions
2 October – Class Discussion
Roughly one reading per class. Do not wait until the day before!
  Srinivasan et al. “Optimizing pipelines for power and performance”
  Mahlke et al. “A comparison of full and partial predicated execution support for ILP processors”
  Palacharla et al. “Complexity-effective superscalar processors”
  Yeh et al. “Two-level adaptive training branch prediction”

## Slide 3
ECE552 Administrivia
4 October – Midterm Exam
  75 minutes, in-class
  Closed book, closed notes exam
  Performance metrics – performance, power, yield
  Technology – trends that changed architectural design
  History – Instruction sets (accumulator, stack, index, general-purpose)
  CISC – microprogramming, writing microprogram fragments
  Pipelining – Performance, hazards and ways to resolve them
  Instruction-level Parallelism – mechanisms to dynamically detect data dependences and to manage instruction flow (Scoreboard, Tomasulo, Physical Register File)
  Speculative Execution – exception handling, branch prediction
  Readings – High-level questions, not details

## Slide 4
Tomasulo’s Implementation
Decode stage allocates instruction template (i.e., tag t) and stores tag in register file.
When instruction completes, tag is de-allocated.
Load
Unit
FU
FU
Store
Unit
< t, result >
Ins# use exec op p1 src1 p2 src2
t1
t2
.
.
tn
Renaming Table & Register File
Reorder Buffer

## Slide 5
Tomasulo’s Structures
Reorder Buffer (ROB) -- buffers in-flight instructions in program order
-- supports in-order commit, precise exceptions
-- e.g., instruction#, use, exec, op
Reservation Stations -- tracks renamed source operands
-- if operands ready, contains value (e.g., v1)
-- if operands pending, contains tag (e.g., t1)
-- may be combined with ROB (e.g., our example)
-- may be distributed across functional units
Renaming Table -- if write committed, points to register file (e.g., F1)
-- if write pending, points to ROB entry (e.g., t1)
-- Rename registers (e.g., F1) with ROB tags (e.g., t1)
Register File -- contains architected state, committed values
Common Data Bus (CDB) -- functional units broadcast computed values
-- broadcast includes <tag, result>

## Slide 6
Tomasulo’s Pipeline
Fetch
Dispatch -- Decode instruction
-- Stall if structural hazard in ROB
-- Allocate ROB entry and rename using ROB tags
-- Read source operands when they are ready
Execute -- Issue instruction when all operands ready
-- Instructions may issue out-of-order
Complete -- Stall if structural hazard on the common data bus
-- Broadcast tag and completed result
-- Mark ROB entry as complete
-- Instructions may complete out-of-order
Retire -- Stall if oldest instruction (head of ROB) not complete
-- Handle any interrupts
-- Write-back value for oldest instruction to register file or mem
-- Free ROB entry
-- Instructions retire in-order

## Slide 7
Physical Register File
Tomasulo Performance Limitations
-- Too much data movement on common data bus
-- Multi-input multiplexors, long buses impact clock frequency
Alternative Approach to Register Renaming
-- Eliminate architectural register file (e.g., R0-R31, F1-F8)
-- Add larger physical register file, which holds all values (e.g., P0-Pn, n>>32)
-- Modify rename table to map architected registers to physical registers
-- Add free list to manage unallocated physical registers
-- Reorder buffer tracks ready operands, supports in-order retire, supports free list management (but does not rename)

## Slide 8
Lifetime of Physical Registers
-- Architected registers are those defined by the instruction set architecture
-- Register renaming can be implemented in two ways
-- Rename with buffer tags -- insert speculatively computed values into ROB
-- Rename with physical registers – hold both committed and speculative values
With Architected Registers With Physical Registers
1. ld R1, (R3) ld P1, (Px)
2. add R3, R1, 4 add P2, P1, 4
3. sub R6, R7, R9 sub P3, Py, Pz
4. add R3, R3, R6 add P4, P2, P3
5. ld R6, (R1) ld P5, (P1)
6. add R6, R6, R3 add P6, P5, P4
7. st R6, (R1) st P6, (P1)
8. ld R6, (R11) ld P7, (Pw)
-- Every instruction’s destination register R renamed to physical register P
-- When do we reuse physical register? When next write of same architected register commits. Example: Reuse P2 when instruction 4 commits

## Slide 9
Physical Register Management
Rename Table
-- Maps architected registers (e.g., R*) to physical registers (e.g., P*)
-- Rename table identifies physical register P* that contains the value of R*
-- Example: MIPS has 32 architected registers so rename table has 32 entries.
-- Microarchitecture might have N >> 32 physical registers.
Physical Registers
-- Contain N>>32 registers that can hold committed data.
-- Committed data is present when “p” flag is set.
Free List
-- List of physical registers available for renaming.
-- Stall pipeline if there are insufficient physical registers
Reorder Buffer
-- Issue logic checks buffer to determine if operand values present
-- Tracks sequence of renamings for the same architected register

## Slide 10
Physical Register Management
-- After the fetch stage, instruction enters decode stage.
-- Decode stage (1) extracts architected registers, (2) renames to physical registers, and (3) inserts instruction into reorder buffer.
Every instruction’s destination register is renamed! Eliminates WAW/WAR hazards.
Renaming for instruction “op Rd, R1, R2” requires the following steps:
Lookup source registers (R1,R2) in rename table.
Insert corresponding physical register (P<y>,P<z>) into ROB.
ii. If values for P<y>, P<z> are present, set “p” flag in ROB.
iii. Lookup destination register (Rd) in rename table.
Suppose Rd already renamed to P<w>.
Because we rename Rd in step iii, this is the last instruction for which P<w> is valid.
Denote P<w> as last physical register (LPRd) in ROB. Required for managing free list.
iv. Rename Rd to P<x>, which is next available register from free list.
Denote as current physical register (PRd) in ROB.
Issue logic sends instruction to execution units when both source registers present

## Slide 11
Renaming R1 to P0
op
p1
PR1
p2
PR2
ex
use
Rd
PRd
LPRd
ROB
1. ld R1, 0(R3)
2. add R3, R1, 4
3. sub R6, R7, R6
4. add R3, R3, R6
5. ld R6, 0(R1)
Free List
P0
P1
P3
P2
P4
<R6>
P5
<R7>
P6
<R3>
P7
P0
Pn
P1
P2
P3
P4
Physical Regs
p
p
p
<R1>
P8
p
X ld p P7 R1 P0
R5
P5
R6
P6
R7
R0
P8
R1
R2
P7
R3
R4
Rename Table
P0
P8
PR1/2: src physical regs
p1/2: set when physical reg values are present
Rd: dest architected reg
LPRd: last dest physical reg
PRd: new dest physical reg

## Slide 12
Renaming R3 to P1
op
p1
PR1
p2
PR2
ex
use
Rd
PRd
LPRd
ROB
1. ld R1, 0(R3)
2. add R3, R1, 4
3. sub R6, R7, R6
4. add R3, R3, R6
5. ld R6, 0(R1)
Free List
P0
P1
P3
P2
P4
<R6>
P5
<R7>
P6
<R3>
P7
P0
Pn
P1
P2
P3
P4
Physical Regs
p
p
p
<R1>
P8
p
x ld p P7 R1 P0
R5
P5
R6
P6
R7
R0
P8
R1
R2
P7
R3
R4
Rename Table
P0
P8
P7
P1
x add P0 R3 P1
PR1/2: src physical regs
p1/2: set when physical reg values are present
Rd: dest architected reg
LPRd: last dest physical reg
PRd: new dest physical reg

## Slide 13
Renaming R6 to P3
op
p1
PR1
p2
PR2
ex
use
Rd
PRd
LPRd
ROB
1. ld R1, 0(R3)
2. add R3, R1, 4
3. sub R6, R7, R6
4. add R3, R3, R6
5. ld R6, 0(R1)
Free List
P0
P1
P3
P2
P4
<R6>
P5
<R7>
P6
<R3>
P7
P0
Pn
P1
P2
P3
P4
Physical Regs
p
p
p
<R1>
P8
p
x ld p P7 R1 P0
R5
P5
R6
P6
R7
R0
P8
R1
R2
P7
R3
R4
Rename Table
P0
P8
P7
P1
x add P0 R3 P1
P5
P3
x sub p P6 p P5 R6 P3
PR1/2: src physical regs
p1/2: set when physical reg values are present
Rd: dest architected reg
LPRd: last dest physical reg
PRd: new dest physical reg

## Slide 14
Renaming R3 to P2
op
p1
PR1
p2
PR2
ex
use
Rd
PRd
LPRd
ROB
1. ld R1, 0(R3)
2. add R3, R1, 4
3. sub R6, R7, R6
4. add R3, R3, R6
5. ld R6, 0(R1)
Free List
P0
P1
P3
P2
P4
<R6>
P5
<R7>
P6
<R3>
P7
P0
Pn
P1
P2
P3
P4
Physical Regs
p
p
p
<R1>
P8
p
x ld p P7 R1 P0
R5
P5
R6
P6
R7
R0
P8
R1
R2
P7
R3
R4
Rename Table
P0
P8
P7
P1
x add P0 R3 P1
P5
P3
x sub p P6 p P5 R6 P3
P1
P2
x add P1 P3 R3 P2
PR1/2: src physical regs
p1/2: set when physical reg values are present
Rd: dest architected reg
LPRd: last dest physical reg
PRd: new dest physical reg

## Slide 15
Renaming R6 to P4
op
p1
PR1
p2
PR2
ex
use
Rd
PRd
LPRd
ROB
1. ld R1, 0(R3)
2. add R3, R1, 4
3. sub R6, R7, R6
4. add R3, R3, R6
5. ld R6, 0(R1)
Free List
P0
P1
P3
P2
P4
<R6>
P5
<R7>
P6
<R3>
P7
P0
Pn
P1
P2
P3
P4
Physical Regs
p
p
p
<R1>
P8
p
x ld p P7 R1 P0
R5
P5
R6
P6
R7
R0
P8
R1
R2
P7
R3
R4
Rename Table
P0
P8
P7
P1
x add P0 R3 P1
P5
P3
x sub p P6 p P5 R6 P3
P1
P2
x add P1 P3 R3 P2
x ld P0 R6 P4
P3
P4
PR1/2: src physical regs
p1/2: set when physical reg values are present
Rd: dest architected reg
LPRd: last dest physical reg
PRd: new dest physical reg

## Slide 16
Physical Register Management
op
p1
PR1
p2
PR2
ex
use
Rd
PRd
LPRd
ROB
x ld p P7 R1 P0
x add P0 R3 P1
x sub p P6 p P5 R6 P3
x ld p P7 R1 P0
1. ld R1, 0(R3)
2. add R3, R1, 4
3. sub R6, R7, R6
4. add R3, R3, R6
5. ld R6, 0(R1)
Free List
P0
P1
P3
P2
P4
<R6>
P5
<R7>
P6
<R3>
P7
P0
Pn
P1
P2
P3
P4
Physical Regs
p
p
p
<R1>
P8
p
R5
P5
R6
P6
R7
R0
P8
R1
R2
P7
R3
R4
Rename Table
P0
P8
P7
P1
P5
P3
P1
P2
x add P1 P3 R3 P2
x ld P0 R6 P4
P3
P4
Execute & Commit
p
p
p
<R1>
P8
x

## Slide 17
Physical Register Management
op
p1
PR1
p2
PR2
ex
use
Rd
PRd
LPRd
ROB
x sub p P6 p P5 R6 P3
x add P0 R3 P1
x add P0 R3 P1
1. ld R1, 0(R3)
2. add R3, R1, 4
3. sub R6, R7, R6
4. add R3, R3, R6
5. ld R6, 0(R1)
Free List
P0
P1
P3
P2
P4
<R6>
P5
<R7>
P6
<R3>
P7
P0
Pn
P1
P2
P3
P4
Physical Regs
p
p
p
P8
x x ld p P7 R1 P0
R5
P5
R6
P6
R7
R0
P8
R1
R2
P7
R3
R4
Rename Table
P0
P8
P7
P1
P5
P3
P1
P2
x add P1 P3 R3 P2
x ld P0 R6 P4
P3
P4
Execute & Commit
p
p
p
<R1>
P8
x
p
p
<R3>
P7

## Slide 18
Active Instruction Window in ROB
ld r1, (r3)
add r3, r1, r2
sub r6, r7, r9
add r3, r3, r6
ld r6, (r1)
add r6, r6, r3
st r6, (r1)
ld r6, (r1)
(newer instructions)
(older instructions)
Cycle (t)
…
ld r1, (r3)
add r3, r1, r2
sub r6, r7, r9
add r3, r3, r6
ld r6, (r1)
add r6, r6, r3
st r6, (r1)
ld r6, (r1)
…
Commit
Fetch
Cycle (t + 1)
Execute

## Slide 19
Superscalar Register Renaming
-- During decode, instruction is allocated new physical register for dest
-- Instruction’s source registers renamed to physical register with newest value
-- Execution unit only sees physical register numbers.
-- Does this work?
Rename Table
Op
Src1
Src2
Dest
Op
Src1
Src2
Dest
Register Free List
Op
PSrc1
PSrc2
PDest
Op
PSrc1
PSrc2
PDest
Update
Mapping
Inst 1
Inst 2
Read Addresses
Read Data
Write Ports

## Slide 20
Superscalar Register Renaming
Rename Table
Op
Src1
Src2
Dest
Op
Src1
Src2
Dest
Register Free List
Op
PSrc1
PSrc2
PDest
Op
PSrc1
PSrc2
PDest
Update
Mapping
Inst 1
Inst 2
Read Addresses
Read Data
Write Ports
=?
=?
Must check for RAW hazards between instructions issuing in same cycle. If RAW hazard, pass Inst1’s Pdest to Inst2’s PSrc1 or PSrc2.

## Slide 21
Memory Dependencies
st r1, j(r2)
ld r3, k(r4)
When can we execute the load?

## Slide 22
In-Order Memory Queue
Execute all loads and stores in program order
Load and store cannot leave ROB and commit architected state until all previous loads and stores have completed execution
Can still execute loads speculatively and out-of-order with respect to other instructions.

## Slide 23
Out-of-order Loads
Conservative out-of-order load execution
st r1, j(r2)
ld r3, k(r4)
-- Split execution of store instruction into two phases
-- Address calculation and data write
-- Can execute load before store if addresses known and j(r2) != k(r4)
-- Each load address compared with addresses of previous uncommitted stores
-- Don’t execute load if any previous store address not known

## Slide 24
Speculative Loads
st r1, j(r2)
ld r3, k(r4)
-- Guess that j(r4) != k(r2)
-- Execute load before store address is known
-- Need to hold all completed but uncommitted load/store addresses in program order
-- Later, if we find r4 == r2, squash load and all following instructions
-- Large penalty for inaccurate address speculation

## Slide 25
Speculative Stores
Just like register updates, stores should not modify the memory until after the instruction is committed.
A speculative store buffer is a structure introduced to hold speculative store data

## Slide 26
Speculative Store Buffer
-- On store execute: mark entry valid (V) and speculative (S), save data and tag of instruction
-- On store commit: clear speculative bit and eventually move data to cache
-- On store abort: clear valid bit
Data
Load Address
Tags
Store Commit Path
L1 Data Cache
Load Data
Tag
Data
S
V
Tag
Data
S
V
Tag
Data
S
V
Tag
Data
S
V
Tag
Data
S
V
Tag
Data
S
V

## Slide 27
Speculative Store Buffer
-- If data in both store buffer and cache, which should we use?
-- Speculative store buffer
-- If same address in store buffer twice, which should we use?
-- Youngest store that is older than load
Data
Load Address
Tags
Store Commit Path
L1 Data Cache
Load Data
Tag
Data
S
V
Tag
Data
S
V
Tag
Data
S
V
Tag
Data
S
V
Tag
Data
S
V
Tag
Data
S
V

## Slide 28
Speculative Datapath
Fetch
Decode & Rename
Reorder Buffer
PC
Branch
Prediction
Update predictors
Commit
Branch
Resolution
Branch
Unit
ALU
Reg. File
MEM
Store Buffer
D$
Execute
kill
kill
kill
kill

## Slide 29
Branch Prediction
Motivation
-- Branch penalties limit performance of deeply pipelined processors
-- Modern branch predictors have high accuracy (>95%) and can significantly reduce branch penalties
Hardware Support
-- Prediction structures: branch history tables, branch target buffer, etc.
-- Mispredict recovery mechanisms:
-- Separate instruction execution and instruction commit
-- Kill instructions following branch in pipeline
-- Restore architectural state to correct path of execution

## Slide 30
Static Branch Prediction
On average, probability a branch is taken is 60-70%.
But branch direction is a good predictor.
ISA can attach preferred direction semantics to branches (e.g., Motorola MC8810, bne0 prefers taken, beq0 prefers not taken).
ISA can allow choice of statically predicted direction (e.g., Intel IA-64). Can be 80% accurate.
JZ
JZ
backward
90%
forward
50%

## Slide 31
Dynamic Branch Prediction
Learn from past behavior
Temporal Correlation -- The way a branch resolves may be a good predictor of the way it will resolve at the next execution
Spatial Correlation -- Several branches may resolve in a highly correlated manner (preferred path of execution in the application)

## Slide 32
2-bit Branch Predictor
Use two-bit saturating counter.
Changes prediction after two consecutive mistakes.

## Slide 33
Branch History Table (BHT)
BHT is an array of 2-bit branch predictors, indexed by branch PC
4K-entry branch history table, 80-90% accurate
0
0
Fetch PC
Branch?
Target PC
+
I-Cache
Opcode
offset
Instruction
k
BHT Index
2k-entry
BHT,
2 bits/entry
Taken/¬Taken?

## Slide 34
Two-Level Branch Prediction
Pentium Pro uses the result from the last two branches
to select one of the four sets of BHT bits (~95% correct)
0
0
k
Fetch PC
Shift in
Taken/¬Taken
results of each branch
2-bit global branch history shift register
Taken/¬Taken?

## Slide 35
Branch Target Buffer (BTB)
BHT only predicts branch direction (taken, not taken). Cannot redirect instruction flow until after branch target determined.
Store target with branch predictions.
During fetch – if (BP == taken) then nPC=target, else nPC=PC+4
Later – update BHT, BTB
IMEM
PC
Branch
Target
Buffer
(2k entries)
k
BPb
predicted
target
BP
target

## Slide 36
Branch Target Buffer (BTB) – v2
Keep both branch PC and target PC in the BTB
If match fails, PC+4 is fetched
Only taken branches and jumps held in BTB
I-Cache
PC
k
Valid
valid
Entry PC
=
match
predicted
target
target PC

## Slide 37
Mispredict Recovery
In-order execution
  No instruction following branch can commit before branch resolves
  Kill all instructions in pipeline behind mis-predicted branch
Out-of-order execution
  Multiple instructions following branch can complete before one branch resolves

## Slide 38
In-order Commit
  -- Instructions fetched, decoded in-order (entering the reorder buffer -- ROB)
  -- Instructions executed out-of-order
  -- Instructions commit in-order (write back to architectural state)
  -- Temporary storage needed in ROB to hold results before commit
Fetch
Decode
Execute
Commit
Reorder Buffer
In-order
In-order
Out-of-order
Kill
Kill
Kill
Exception?
Inject handler PC

## Slide 39
Branch Misprediction in Pipeline
  -- Can have multiple unresolved branches in reorder buffer -- ROB
  -- Can resolve branches out-of-order by killing all instructions in ROB that follow a mispredicted branch
Fetch
Decode
Execute
Commit
Reorder Buffer
Kill
Kill
Kill
Branch
Resolution
Inject correct PC
Branch
Prediction
PC
Complete

## Slide 40
Mispredict Recovery
  Take snapshot of register rename table at each predicted branch, recover earlier snapshot if branch mispredicted
t
v
t
v
t
v
Register File
Reorder
Buffer
Load
Unit
FU
FU
FU
Store
Unit
< t, result >
t1
t2
.
.
tn
Ins# use exec op p1 src1 p2 src2 pd dest data
Commit
Rename
Table
r1
t
v
r2
Rename
Snapshots
Ptr2 next to commit
Ptr1 next available
rollback next available

## Slide 41
Acknowledgements
    These slides contain material developed and copyright by
    Arvind (MIT)
    Krste Asanovic (MIT/UCB)
    Joel Emer (Intel/MIT)
    James Hoe (CMU)
    John Kubiatowicz (UCB)
    Alvin Lebeck (Duke)
    David Patterson (UCB)
    Daniel Sorin (Duke)